## Slide 1
3D CAD

## Slide 2
3D Modelling- Extrude, Revolve, Fillet Etc.
3D Modelling- Advantages
Animation & Simulation- Advantages
Learning Intentions

## Slide 3
3D Modelling- Extrude
The extrusion tool is used to add depth to a sketch to transform it into a 3D model as shown below
Extrude
Join: Adds the volume created by the extruded feature to another feature or body.
Cut: Removes the volume created by the extruded feature from another feature or body.

## Slide 4
Revolve
Revolve
Creates a 3d model or feature by revolving a profile around an axis.
Axis is the centre line you want to revolve round
Profile is the sketch
3D Modelling- Revolve

## Slide 5
Shell
The shell tool allows you to remove surfaces and hollow out any shape or feature.
Fillet
The fillet tool allows you to round any selected corner or edge on a model.
Chamfer
The chamfer tool allows you to remove an angular section along any selected corner or edge.
3D Modelling- Alterations

## Slide 6
3D Modelling- Advantages
Models can be easily sent electronically all over the world
Components can be used in different projects
Ease of modification- can be changed easily
Ease of storage- as opposed to large scale models

## Slide 7
Computer Animation
Computer Simulation
Animation & Simulation

## Slide 8
Animation - Advantages
Safer
No risk of crashing for driver
Cheaper
No running cost
e.g. petrol or new parts
Testing
Can be tested to see how it would cope in a crash situation
Example: Race Car