## Slide 1: S3 Cad Modelling Solutions
Questions 1 – 3

## Slide 3: Question 1
Sketch the shape shown using the line tool. (1 mark – ALL sizes must be shown to gain mark)
Extrude (addition) (1 mark) 180mm (1 mark)
Shell the shape removing the top surface (1 mark) thickness of 10mm (1 mark)
Sketch a circle Ø45 centred on the front surface (1 mark)
Extrude the circle (subtract) (1 mark) 10mm (1 mark)
Let’s watch this being modelled in the video on the next slide.

## Slide 6: Question 2
Sketch a circle Ø65. (1 mark)
Extrude (addition) (1 mark) 22mm (1 mark)
On one side, sketch a circle Ø16 (1 mark)
Extrude (subtraction) (1 mark) 10mm (1 mark)
On the opposite side, sketch a circle Ø8 (1 mark)
Extrude (subtraction) (1 mark) through all material / 22mm (1 mark)
Fillet the outer edges of the wheel 8mm (1 mark)
Note that the two circles can be drawn and extruded in the opposite order to how it is described here – it doesn’t matter in this case i.e. the 8mm circle can be drawn first. You will see this in the video on the next slide.

## Slide 9: Question 3
Sketch the shape shown using the line tool. (1 mark – ALL sizes must be shown to gain mark)
Extrude (addition) (1 mark) 50mm (1 mark)
Sketch a circle Ø30 (1 mark) in the position shown (sketch must show dimensions of the position of the circle 1 mark)
Extrude (subtraction) (1 mark) through all material / 100mm (1 mark)
Fillet the short vertical edges (1 mark) 25mm (1 mark)
Let’s watch this being modelled in the video on the next slide.