N4 Electricity & Energy revision checklist

Generation of electricity

- Advantages and disadvantages of different methods of electricity generation and distribution.

- The potential role of different methods of electricity generation in future sustainable energy supply.

- The concept of energy efficiency and energy efficiency issues related to generation, distribution and use of electricity.

Electrical power

- Electrical power as a measure of the energy transferred electrically by an appliance every second.

- Power consumption of different appliances, qualitative and quantitative.

- Use of the appropriate relationship between power, energy and time to justify energy saving measures.

- Energy efficiency as a key factor in energy generation, distribution and use.

- Calculation of efficiency given input and output power/energy.

Electromagnetism

- Relationship between electricity and magnetism.

- Practical applications of magnets and electromagnets.

Practical electrical and electronic circuits

- Measurement of current, voltage and resistance using appropriate meters in series or parallel circuits.

- Identification and use a range of electrical and electronic components to construct practical electronic circuits and systems.

- Current and voltage relationships in a series circuit.

- Practical applications of series and parallel circuits.

- Qualitative factors that affect resistance. Use of the appropriate relationships between voltage, current and resistance in calculations for series circuits.

Gas laws and the kinetic model

- Kinetic model of a gas

- Applications of the kinetic model of a gas using knowledge of pressure, volume and temperature (for a fixed mass of gas).

Generating Electricity

There are many different methods of generating electricity

Non-renewables

Nuclear power

Coal fired generators

Gas fired generators

Oil fired generators

Renewables

Hydro-electric schemes

Geothermal

Wave

Wind

Biomass

Photovoltaic – Turns light directly into electricity.

Non-renewable sources have the advantages that they can generate a lot of energy from a power station and they are always available. They have the disadvantages that they generate waste which can be dangerous or polluting and their source of energy will run out.

Renewables have the advantages that they do not produce polluting waste and they will not run out. They have the disadvantages that they are often weather dependent, cost a lot to build, each generator does not produce a lot of energy and some take up a lot of land space.

Energy Conversions

Electrical appliances use the electrical energy from the mains supply and batteries and convert (change) it into another form of energy like sound, light, kinetic (movement) and heat.

Example

The motor in a washing machine changes electrical energy into kinetic energy.

Efficiency

When one form of energy is turned into another some energy is lost every time there is a change. Coal fired power stations are less than 40% efficient.

When power is sent down electricity cables some energy is lost. Less energy is lost if the power is transmitted at a high voltage and low current. This is achieved by using transformers which change low voltage into high voltage at the power station end then again at the town end where the high voltage is changed back into safe low voltage of 230 volts.

Electrical Power

Power is the work or energy done or used by a device in one second. It is measured in Watts.

Power = Energy ÷ time

Example

If an electric fire uses 600,000J of energy in a time of 5 minutes, calculate the power output of the fire. Ensure that all quantities are stated with the correct units.

P = ?

E = 600000

t = 5min = 300s

Power = Energy ÷ time

= 600000/300

= 2000W

Devices which make heat usually use much more energy than others and so have a higher power rating. Eg kettles have a power of about 2000 watts, but a computer monitor has a power consumption of about 40 watts.

The efficiency of a device is a measure of how well it converts electricity into other forms of energy.

% efficiency = (useful Energy out ÷ Energy in) x 100

and

% efficiency = (useful Power out ÷ Power in) x 100

Example

A light bulb gives out 10 watts of light while using 25 watts of electrical energy. What is the efficiency of the light bulb?

Useful Power out = 10 watts

Power in = 25 watts

% efficiency = (useful Power out ÷ Power in) x 100

= (10÷35)x100

= 0.286x100

= 28.6 %

Magnetism

Permanent magnets are pieces of material, often iron, which have a magnetic field round them. If you suspend a magnet on a thread it will line up along the Earth’s magnetic field (North – South). This is one of the ways the Vikings navigated. It is how a compass works.

Permanent magnets are used to temporarily hold things in place like door catches. They can be part of small electric motors and loudspeakers.

Electromagnets

An electromagnet is simply a coil of wire wound round a metal core.

The strength of the magnet depends on the number of coils of wire, the type of iron core and the voltage applied to the coil.

Anything with an electric motor has an electromagnet as part of the motor. Electromagnets are also used to lift iron or steel objects. They are used to hold fire doors inside buildings open and automatically let them close in the event of a fire. Most loudspeakers have an electromagnet which makes the speaker vibrate.

Generators are made of a coil of wire turning inside an electromagnet.

The voltage generated depends on the strength of the electromagnet, the number of coils in the field windings and the speed of the turning coil.

## Electrical Circuits

## Measuring Current and Potential Difference or Voltage

Electric current is measured using an ammeter which is connected in series with the component. Potential difference (p.d.), or voltage, is measured using a voltmeter which is connected in parallel with the component.

Current and Potential Difference or Voltage in Series Circuits

The current is the same at all points in a series circuit. The sum of the potential differences across the components in a series circuit is equal to the voltage of the supply.

Series circuits are often used as a safety feature. In a series circuit with a number of switches all switches have to be closed for the circuit to work. Eg. For your TV to come on the switch at the fuse box has to be on, the switch at the wall has to be on, if there is a switchable multi-block it has to be switched on then the TV itself has to be switched on. All together 4 switches if any one is off your TV will not work.

## Current and Potential Difference or Voltage in Parallel Circuits

The potential difference across components in parallel is the same for all components. The sum of the currents in parallel branches is equal to the current drawn from the supply.

Electrical Resistance

Resistance is a measure of the opposition of a circuit component to the flow of charge or current through that component. The greater the resistance of a component, the less will be the current through that component. All normal circuit components have resistance and the resistance of a component is measured using the relationship:

Most circuits are wired in parallel. This is so that if one thing blows the rest stay on. It also means that everything connected in parallel will have the same voltage.

Resistance = voltage ÷ current

| Symbols | Units |
| --- | --- |
| I = electric current | measured in amperes, A |
| V = potential difference or voltage | measured in volts, V |
| R = resistance | measured in ohms, Ω |

This relationship is known as Ohm’s Law, named after a German physicist, Georg Ohm. For components called resistors, the resistance remains approximately constant for different values of current therefore the ratio V/I (= R) remains constant for different values of current.

In some components which get hot the resistance changes with temperature. The hotter a light bulb the greater the resistance.

Example

Calculate the resistance of the resistor in the diagram opposite.

Ensure that all quantities are stated in the correct units.

R = ?

V = 5V

I = 200mA = 0.2A

Resistance = voltage ÷ current

= 5÷0.2

= 25 (

Ohmmeters can also measure resistance of components.

Electrical Components

| Cell |  | Supplies electrical energy to a circuit. | To power low power consumption mobile devices |
| --- | --- | --- | --- |
| Battery |  | Supplies more electrical energy than a cell. | To power mobile devices which require more energy |
| Lamp |  | To convert electrical energy into light energy | To light up objects or as an indicator that something is on |
| Switch |  | To control the operation of circuits | In any circuit which needs switched on and off |
| Resistor |  | To control the flow of current or the value of voltage | Used in any circuit where different currents or voltages are required. |
| Variable resistor |  | To vary the flow of current or the value of voltage | Used in any circuit where changing currents or voltages are required. Eg a volume control or dimmer switch. |
| Voltmeter |  | To measure the voltage in a circuit | In monitoring devices where a physical change is turned into a voltage. Eg a speedometer. |
| Ammeter |  | To measure the current in a circuit | In monitoring devices where a physical change is turned into a current. Eg a speedometer. |
| Light Emitting Diode |  | To convert electrical energy into light energy | Most often as on/off indicators but now more and more as high efficiency lighting |
| Motor |  | To convert electrical energy into movement energy | A washing machine |
| Microphone |  | To convert sound energy into electrical energy | A public address system |
| Loudspeaker |  | To convert electrical energy into sound energy | A public address system |
| Fuse |  | In the case of a fault to protect a circuit from too much current | In any device where a fault could result in too much current |
| Thermistor |  | A device who’s resistance varies with temperature | In circuits where temperature has to be monitored and controlled eg a fish tank |
| Light Dependent Resistor |  | A device who’s resistance varies with light level | In circuits where light levels have to be monitored and controlled eg a green house |
| And Gate |  | A device which gives an output if there are two inputs. | In a burglar alarm system where the system is switched on and a sensor is activated. |
| Or Gate |  | A device which gives an output if either input is on | In a car to switch on the courtesy light if any door is opened. |

Gas Laws

The kinetic model of a gas explains the pressure of a gas in terms of the movement of the gas particles.  Every time a gas particle hits the wall of a container it exerts a small amount of force on the wall.  The sum of all these small forces acting on the area of the walls gives the pressure of the gas.

If you heat the particles of a gas they move faster, hit the walls of the container harder and more often creating more pressure – T increases, P increases, (V constant).

If you heat some gas which is not tightly contained the particles move fast and spread out taking up more volume – T increases, V increases, (P constant).

If you squeeze a gas the volume gets smaller but the particles hit the walls of the container more often so making the pressure greater – V decreases, P increases, (T constant).

# Text boxes

Electricity & Energy

St Luke’s High School

National 4 Physics

Name :     ___________________

Teacher :  ___________________

Room :     _______

All use generators to make electricity

Permanent magnet field pattern