# Anthropometrics

Anthropometrics deals with the relationships between the dimensions of the user and those of the object. These relationships are of three basic kinds:

- Clearance

- Reach

- Posture

Clearance (head room, knee room, elbow room, etc.) must be adequate to accommodate the bodily dimensions of a large-sized member of the user population. In these cases, anthropometric data allow us to specify the minimum dimension acceptable in the object. Hence the height of a table (underside) should not be less than the knee height of a 95th percentile user.

Reach dimensions, on the other hand, should be based on a small member of the population. They allow us to specify the maximum dimension allowable in the object. Hence the height of a seat should not be greater than than the lower leg length of a 5th percentile user. (This particular dimension is usually called popliteal height since anatomists call the back of the knee the popliteal region.)

Postural problems are often more complicated than those of clearance and reach. For example, if we wanted to work out the height of a kitchen worktop, it is not obvious whether we should design for tall or short people. 9Various studies have shown that such a worktop should be between 50mm and 100mm below the elbow height of the user when standing.) We should select the worktop height which “accommodates” the greatest possible proportion of the target population. Worktop height should be 75mm below the elbow height of the average user. If the height which is chosen falls outside the desirable limits for a significant proportion of the population, we have to decide whether the problems arising from a worktop which is too high are worse than those arising from one which is too low. This might lead us to shift our planned height upward or downward in order to achieve the best possible compromise. Or we may conclude that an adjustable worktop is required.

Group A Heights of principal anatomical landmarks

- Stature

The height of the fully erect standing person. Clearance from floor to head obstacles. Stature is an important reference dimension for comparing populations.

- Eye height

The eye level of the standing person. Defines the centre of the visual field and is an important reference level for the location and design of visual displays.

- Shoulder height (Acromial)

The height of the acromion – the bony ‘point’ of the shoulder. It approximately defines the centre of rotation of the shoulder joint and may be used with dimensions 18 & 23 for calculating zones of reach.

- Elbow height

Reference level for determining the heights of working surfaces.

- Hip height (Trochanteric)

Height of the greater trochanter (a bony prominence at the top of the thigh bone). Defines the centre of rotation of the hip joint and the functional length of the lower limb. The level at which loads are commonly carried.

- Knuckle height

Reference level for hand grips. For support (handrails,etc.) a level some 100mm above knuckle height is desirable. Handholds on objects for carrying should be at less than knuckle height. Lowest acceptable level for most types of hand operated controls. Optimum height for lifting actions (an average value of 750mm is often quoted).

- Fingertip height

Lowest acceptable height for fingertip operated controls

# Group B Sitting Dimensions

8. Sitting Height

Vertical distance of the crown of the head above the seat surface. Clearance from seat to overhead obstacles for sitting person. Add 10mm for thick clothing beneath buttocks, 25mm for hat and 35mm for safety helmet.

- Sitting eye height

Eye level of the sitting person above the seat surface. Reference level for the location of visual displays. Subtract up to 40mm for sitting slump.

- Sitting shoulder height (Acromial)

Shoulder level of the sitting person above the seat surface. Subtract up to 40mm for sitting slump.

- Sitting elbow height

The height of the underside of the elbow above the seat. Suitable height for armrests in many seats. Reference level for table heights, etc, keyboards should be at elbow height, writing surfaces should be 50mm to 100mm above elbow height.

- Thigh thickness

Vertical distance from the seat surface to the higher part of the thigh. Clearance required between seat and underside of table or other obstacle. This dimension interacts strongly with elbow rest height.

- Buttock-knee length

Horizontal distance from the back of the uncompressed buttocks to the front of the knee in the standard sitting position. Clearance required between seat back and obstacles in front of the knee. Add correction for outdoor clothing.

- Buttock-popliteal length

Horizontal distance from the uncompressed buttocks to the popliteal fossa (the back of the knee) in the standard sitting position. Maximum acceptable depth of a seat.

- Knee height

Height of the top of the knee from the floor in the standard sitting position. Clearance required beneath tables, etc. Add correction for shoes.

- Popliteal height

Height of the popliteal fossa (the back of the knee) from the floor in the standard sitting position. Defines the maximum acceptable height of a seat. The optimum height of a seat is commonly quoted as 25mm to 50mm below popliteal height. Add correction for shoes.

- Shoulder breadth (Bideltoid)

Maximum breadth across the shoulders. Clearance required in upper part of work space. Add correction for outdoor clothing.

- Biacromial breadth

Horizontal distance between the acromia (the bony ‘points’ of the shoulders). Defines centre of rotation of upper limbs.

- Elbow-elbow breadth

Maximum lateral distance across the elbows while the arms hang loosely by the sides. Clearance required at elbow height. Add correction for outdoor clothing.

- Hip breadth

Maximum lateral distance across the hips. Clearance required at seat height (between the arms of chairs). A very obese person may have a hip breadth of 550mm. Add correction for outdoor clothing. The breadth of a seat which does not have arms, may comfortably be 50mm less than hip breadth.

- Span

Lateral distance between the fingertips when both arms are stretched out sideways. Defines the lateral limits of convenient reach.

- Elbow span

Lateral distance between the elbows when both arms are stretched out sideways. A useful dimension when considering ‘elbow room’ in the workspace.

- Standing overhead reach

Height of middle fingertip above the floor when the arm is raised comfortably above the head without stretching. Overhead limit for location of fingertip operated controls. Add correction for shoes. Add 75mm for stretching and another 75mm for standing on tiptoe.

- Sitting overhead reach

Height of middle fingertip above seat surface, when the arm is raised comfortably above the head without stretching. Overhead limit for fingertip operated controls. Add 75mm for stretching.

- Forward reach

Horizontal distance from the back of the shoulder blades to the middle fingertip of the horizontal, forward-reaching upper limb. (The subject raises their arm, they do not thrust their shoulders forward of incline their trunk.) Forward limit for convenient operation of controls. Add 100mm for a forward thrusting action of the shoulders and another 150mm for a 300 inclination of the trunk.

Group D Hand dimensions

- Hand length

From crease of the wrist to the tip of the middle finger.

- Hand breadth (metacarpal)

Overall breadth of the palm at its widest point, ie. Excluding thumb. Clearance required for handgrips, etc. By deliberately contracting the palm, this dimension may be reduced by up to 25mm.

- Hand breadth (including thumb)

Clearance required for hand access.

- Palm length

From the crease of the wrist to the base of the middle finger.

- Index Finger Length

From the web to the fingertip. The middle finger is longer (by about 10mm), the ring finger is about the same length , the little finger is shorter (by about 17mm).

- Index finger breadth

Across the proximal interphalangeal joint (the finger joint nearest to the palm). Clearance required for fingertip access.

- Thumb breadth

Across the joint

- Hand thickness (at palm)

Measured at the thickest point – across the knuckles but excluding  thumb. Clearance required in handgrips, etc.

- Hand thickness (including thumb)

Clearance required for hand access.

- Maximum grip diameter

|  |  | Men | Women |
| --- | --- | --- | --- |
|  |  | 5th %le | 50th %le | 95th %le | 5th %le | 50th %le | 95th %le |
|  | British Adults 19 - 65 years |  |  |  |  |  |  |
|  | Body weight (kg) | 55 | 75 | 95 | 45 | 63 | 81 |
| 1 | Stature | 1625 | 1740 | 1855 | 1510 | 1610 | 1710 |
| 2 | Eye Height | 1515 | 1630 | 1745 | 1405 | 1505 | 1605 |
| 3 | Shoulder Height | 1315 | 1425 | 1535 | 1215 | 1310 | 1405 |
| 4 | Elbow Height | 1005 | 1090 | 1175 | 930 | 1005 | 1080 |
| 5 | Hip Height | 840 | 920 | 1000 | 740 | 810 | 880 |
| 6 | Knuckle Height | 690 | 755 | 820 | 660 | 720 | 780 |
| 7 | Fingertip Height | 590 | 655 | 720 | 560 | 625 | 690 |
| 8 | Sitting Height | 850 | 910 | 970 | 790 | 850 | 910 |
| 9 | Sitting Eye Height | 730 | 790 | 850 | 685 | 740 | 795 |
| 10 | Sitting Shoulder Height | 540 | 595 | 650 | 505 | 555 | 605 |
| 11 | Sitting Elbow Height | 195 | 245 | 295 | 185 | 235 | 285 |
| 12 | Thigh Thickness | 135 | 160 | 185 | 125 | 155 | 185 |
| 13 | Buttock-Knee Length | 545 | 595 | 645 | 520 | 570 | 620 |
| 14 | Buttock-Popliteal Length | 440 | 495 | 550 | 435 | 480 | 530 |
| 15 | Knee Height | 495 | 545 | 595 | 455 | 500 | 545 |
| 16 | Popliteal Height | 390 | 440 | 490 | 355 | 400 | 495 |
| 17 | Shoulder Breadth (bideltoid) | 420 | 465 | 510 | 355 | 395 | 435 |
| 18 | Biacromial breadth | 365 | 400 | 435 | 325 | 355 | 385 |
| 19 | Elbow-Elbow Breadth | 370 | 450 | 530 | 320 | 385 | 450 |
| 20 | Hip Breadth | 310 | 360 | 410 | 305 | 370 | 435 |
| 21 | Chest (Bust) depth | 215 | 250 | 285 | 205 | 250 | 295 |
| 22 | Abdominal depth | 220 | 270 | 320 | 205 | 255 | 305 |
| 23 | Shoulder-Fingertip Length | 720 | 780 | 840 | 650 | 705 | 760 |
| 24 | Shoulder-Elbow Length | 330 | 365 | 400 | 300 | 330 | 360 |
| 25 | Elbow-Fingertip Length | 440 | 475 | 510 | 400 | 430 | 460 |
| 26 | Span | 1655 | 1790 | 1925 | 1490 | 1605 | 1720 |
| 27 | Elbow Span | 870 | 945 | 1020 | 780 | 850 | 920 |
| 28 | Standing Overhead Reach | 2040 | 2170 | 2300 | 1895 | 2010 | 2125 |
| 29 | Sitting Overhead Reach | 1255 | 1355 | 1455 | 1150 | 1255 | 1340 |
| 30 | Forward Reach | 835 | 890 | 945 | 760 | 810 | 860 |
| 31 | Hand Length | 173 | 189 | 205 | 159 | 174 | 189 |
| 32 | Hand Breadth (Metacarpal) | 79 | 87 | 95 | 69 | 76 | 83 |
| 33 | Hand Breadth (including thumb) | 97 | 105 | 113 | 84 | 92 | 100 |
| 34 | Palm Length | 97 | 107 | 117 | 89 | 97 | 105 |
| 35 | Index Finger Length | 64 | 72 | 80 | 60 | 67 | 74 |
| 36 | Index Finger Breadth | 18 | 21 | 24 | 15 | 18 | 21 |
| 37 | Thumb Breadth | 20 | 23 | 26 | 16 | 19 | 22 |
| 38 | Hand Thickness at Palm | 28 | 33 | 38 | 23 | 28 | 33 |
| 39 | Hand Thickness (including thumb) | 44 | 51 | 58 | 40 | 45 | 50 |
| 40 | Maximum grip diameter | 45 | 52 | 59 | 43 | 48 | 53 |

|  |  | Boys | Girls |
| --- | --- | --- | --- |
|  |  | 5th %le | 50th %le | 95th %le | 5th %le | 50th %le | 95th %le |
|  | 15-18 years |  |  |  |  |  |  |
| 1 | Stature | 1610 | 1735 | 1855 | 1520 | 1620 | 1715 |
| 2 | Eye Height | 1490 | 1615 | 1740 | 1410 | 1510 | 1610 |
| 3 | Shoulder Height | 1310 | 1420 | 1530 | 1225 | 1315 | 1405 |
| 4 | Elbow Height | 995 | 1080 | 1170 | 930 | 1005 | 1080 |
| 5 | Hip Height | 835 | 915 | 995 | 750 | 820 | 885 |
| 6 | Knuckle Height | 675 | 745 | 815 | 665 | 720 | 780 |
| 7 | Fingertip Height | 555 | 625 | 695 | 550 | 610 | 665 |
| 8 | Sitting Height | 825 | 900 | 970 | 800 | 855 | 905 |
| 9 | Sitting Eye Height | 715 | 785 | 850 | 690 | 740 | 790 |
| 10 | Sitting Shoulder Height | 520 | 580 | 635 | 500 | 550 | 595 |
| 11 | Sitting Elbow Height | 185 | 235 | 285 | 185 | 230 | 270 |
| 12 | Thigh Thickness | 125 | 150 | 180 | 120 | 145 | 170 |
| 13 | Buttock-Knee Length | 530 | 580 | 630 | 510 | 555 | 600 |
| 14 | Buttock-Popliteal Length | 440 | 490 | 545 | 435 | 480 | 520 |
| 15 | Knee Height | 500 | 545 | 590 | 455 | 500 | 540 |
| 16 | Popliteal Height | 395 | 440 | 485 | 360 | 405 | 445 |
| 17 | Shoulder Breadth (bideltoid) | 385 | 435 | 490 | 360 | 395 | 430 |
| 18 | Biacromal breadth | 345 | 385 | 420 | 330 | 355 | 385 |
| 19 | Elbow-Elbow Breadth |  |  |  |  |  |  |
| 20 | Hip Breadth | 290 | 330 | 375 | 300 | 345 | 385 |
| 21 | Chest depth | 170 | 220 | 265 | 185 | 225 | 265 |
| 22 | Abdominal depth | 190 | 230 | 270 | 185 | 220 | 255 |
| 23 | Shoulder-Fingertip Length | 715 | 780 | 845 | 650 | 700 | 750 |
| 25 | Elbow-Fingertip Length | 435 | 470 | 510 | 395 | 425 | 455 |
| 26 | Span | 1630 | 1785 | 1935 | 1505 | 1610 | 1720 |
| 27 | Elbow Span | 855 | 940 | 1025 | 785 | 850 | 915 |
| 28 | Standing Overhead Reach | 1955 | 2110 | 2260 | 1825 | 1965 | 2110 |
| 29 | Sitting Overhead Reach | 1120 | 1225 | 1330 | 1035 | 1135 | 1235 |
| 30 | Forward Reach | 650 | 725 | 795 | 605 | 670 | 730 |
| 31 | Hand Length | 170 | 190 | 205 | 160 | 175 | 190 |
| 32 | Hand Breadth (Metacarpal) | 80 | 90 | 95 | 70 | 75 | 80 |
| 41 | Foot Length | 240 | 265 | 285 | 220 | 240 | 260 |
| 42 | Foot Breadth | 90 | 100 | 110 | 80 | 90 | 100 |
| 47 | Head Length | 185 | 200 | 210 | 170 | 180 | 190 |
| 48 | Head Breadth | 145 | 155 | 165 | 135 | 145 | 155 |

|  |  | Boys | Girls |
| --- | --- | --- | --- |
|  |  | 5th %le | 50th %le | 95th %le | 5th %le | 50th %le | 95th %le |
|  | 9-14 years |  |  |  |  |  |  |
| 1 | Stature | 1225 | 1475 | 1725 | 1210 | 1445 | 1680 |
| 2 | Eye Height | 1070 | 1340 | 1610 | 1095 | 1330 | 1565 |
| 3 | Shoulder Height | 960 | 1190 | 1420 | 950 | 1165 | 1380 |
| 4 | Elbow Height | 735 | 910 | 1085 | 725 | 895 | 1065 |
| 5 | Hip Height | 620 | 775 | 930 | 610 | 745 | 880 |
| 6 | Knuckle Height | 500 | 625 | 750 | 520 | 640 | 760 |
| 7 | Fingertip Height | 415 | 525 | 635 | 420 | 535 | 650 |
| 8 | Sitting Height | 645 | 765 | 885 | 650 | 765 | 880 |
| 9 | Sitting Eye Height | 535 | 655 | 775 | 540 | 665 | 770 |
| 10 | Sitting Shoulder Height | 395 | 480 | 585 | 380 | 475 | 570 |
| 11 | Sitting Elbow Height | 150 | 205 | 260 | 145 | 205 | 265 |
| 12 | Thigh Thickness | 95 | 130 | 165 | 90 | 125 | 160 |
| 13 | Buttock-Knee Length | 390 | 490 | 590 | 390 | 485 | 580 |
| 14 | Buttock-Popliteal Length | 315 | 405 | 495 | 330 | 410 | 490 |
| 15 | Knee Height | 370 | 465 | 560 | 370 | 450 | 530 |
| 16 | Popliteal Height | 300 | 375 | 450 | 300 | 365 | 430 |
| 17 | Shoulder Breadth (bideltoid) | 280 | 355 | 430 | 275 | 350 | 425 |
| 18 | Biacromal breadth | 270 | 325 | 380 | 260 | 215 | 370 |
| 19 | Elbow-Elbow Breadth |  |  |  |  |  |  |
| 20 | Hip Breadth | 200 | 285 | 340 | 210 | 290 | 370 |
| 21 | Chest depth | 120 | 175 | 230 | 110 | 180 | 250 |
| 22 | Abdominal depth | 145 | 195 | 245 | 145 | 195 | 245 |
| 23 | Shoulder-Fingertip Length | 520 | 645 | 770 | 500 | 625 | 750 |
| 25 | Elbow-Fingertip Length | 320 | 395 | 470 | 310 | 380 | 450 |
| 26 | Span | 1200 | 1495 | 1790 | 1170 | 1435 | 1700 |
| 27 | Elbow Span | 630 | 790 | 950 | 610 | 760 | 910 |
| 28 | Standing Overhead Reach | 1460 | 1785 | 2110 | 1440 | 1755 | 2070 |
| 29 | Sitting Overhead Reach | 830 | 1025 | 1220 | 810 | 1010 | 1210 |
| 30 | Forward Reach | 495 | 615 | 735 | 490 | 600 | 710 |
| 31 | Hand Length | 130 | 160 | 190 | 130 | 155 | 180 |
| 32 | Hand Breadth (Metacarpal) | 60 | 75 | 90 | 60 | 70 | 80 |
| 41 | Foot Length | 185 | 230 | 275 | 185 | 220 | 255 |
| 42 | Foot Breadth | 75 | 90 | 105 | 70 | 85 | 100 |
| 47 | Head Length | 165 | 185 | 205 | 155 | 175 | 195 |
| 48 | Head Breadth | 135 | 150 | 165 | 125 | 140 | 155 |

|  |  | Boys | Girls |
| --- | --- | --- | --- |
|  |  | 5th %le | 50th %le | 95th %le | 5th %le | 50th %le | 95th %le |
|  | 3-8 years |  |  |  |  |  |  |
| 1 | Stature | 930 | 1170 | 1295 | 900 | 1090 | 1280 |
| 2 | Eye Height | 825 | 1055 | 1175 | 800 | 990 | 1180 |
| 3 | Shoulder Height | 735 | 925 | 1025 | 700 | 860 | 1020 |
| 4 | Elbow Height | 550 | 705 | 790 | 530 | 655 | 780 |
| 5 | Hip Height | 415 | 595 | 680 | 410 | 530 | 650 |
| 6 | Knuckle Height | 375 | 480 | 545 | 375 | 465 | 565 |
| 7 | Fingertip Height | 305 | 395 | 460 | 290 | 385 | 480 |
| 8 | Sitting Height | 535 | 640 | 700 | 520 | 605 | 690 |
| 9 | Sitting Eye Height | 430 | 525 | 585 | 405 | 500 | 595 |
| 10 | Sitting Shoulder Height | 315 | 390 | 440 | 300 | 365 | 430 |
| 11 | Sitting Elbow Height | 120 | 170 | 205 | 115 | 145 | 195 |
| 12 | Thigh Thickness | 70 | 95 | 120 | 60 | 90 | 120 |
| 13 | Buttock-Knee Length | 275 | 370 | 420 | 275 | 350 | 425 |
| 14 | Buttock-Popliteal Length | 230 | 305 | 350 | 230 | 295 | 360 |
| 15 | Knee Height | 265 | 360 | 410 | 250 | 325 | 400 |
| 16 | Popliteal Height | 205 | 295 | 340 | 210 | 270 | 330 |
| 17 | Shoulder Breadth (bideltoid) | 235 | 285 | 325 | 230 | 275 | 320 |
| 18 | Biacromal breadth | 205 | 265 | 295 | 205 | 245 | 285 |
| 20 | Hip Breadth | 175 | 215 | 250 | 170 | 215 | 260 |
| 21 | Chest depth | 105 | 140 | 170 | 100 | 135 | 170 |
| 22 | Abdominal depth | 135 | 160 | 185 | 135 | 165 | 195 |
| 23 | Shoulder-Fingertip Length | 395 | 505 | 570 | 370 | 460 | 550 |
| 25 | Elbow-Fingertip Length | 240 | 310 | 345 | 240 | 290 | 340 |
| 26 | Span | 905 | 1160 | 1300 | 860 | 1060 | 1260 |
| 27 | Elbow Span | 475 | 610 | 690 | 450 | 560 | 670 |
| 28 | Standing Overhead Reach | 1030 | 1390 | 1565 | 1030 | 1285 | 1540 |
| 29 | Sitting Overhead Reach | 650 | 810 | 905 | 620 | 750 | 880 |
| 30 | Forward Reach | 370 | 495 | 560 | 365 | 455 | 545 |
| 31 | Hand Length | 100 | 130 | 145 | 100 | 120 | 140 |
| 32 | Hand Breadth (Metacarpal) | 50 | 60 | 70 | 45 | 55 | 65 |
| 41 | Foot Length | 140 | 185 | 210 | 140 | 170 | 200 |
| 42 | Foot Breadth | 60 | 75 | 85 | 50 | 65 | 80 |
| 47 | Head Length | 170 | 180 | 195 | 150 | 165 | 180 |
| 48 | Head Breadth | 130 | 140 | 150 | 125 | 135 | 145 |

Seats and seated workstations

  - Seat height (floor to sitting surface)

The optimum height for working chairs is often said to be 25mm to 50mm below popliteal height – which suggests a range of 380mm (5th percentile woman, shod minus 25mm) to 465mm (95th percentile man, shod, minus 50mm). An adjustable chair should include this range. In practice, people commonly set their chairs higher than this, because of the tables they use. In designing a working chair we must consider the task and the table on which it is performed. The desirable height for an easy chair may well be lower than this since people like to stretch out their legs.

In a non-adjustable seat, these considerations are academic. Seat heights should not exceed the popliteal height of the shortest user – and at more than 25mm above popliteal height, seats rapidly become uncomfortable. A seat which is too high will be more tolerable if its front edge is suitably contoured. Excessively low seats result in slouched postures of the pelvis and lumbar spine, which are both inelegant and unhealthy. The lower a seat, the more difficult it is to stand up and sit down ( a particular problem for elderly or infirm people). The shod popliteal height of a 5th percentile woman (400mm) is a good compromise.

b.) Seat depth (front of sitting surface to backrest)

This should be treated as a reach dimension based on buttock-popliteal length, 5th percentile female = 435mm. Deeper seats will prevent shorter members of the population from fully utilizing the backrest, furthermore they increase the effort required to stand up and sit down. Tall people sometimes complain of seats, particularly easy chairs, being too short. It is not easy to see why – in many cases an inadequate backrest might be to blame.

- Backrest

The function of the backrest is to give support to the weight of the trunk, but it must not impede the movements of the user’s arms. When the latter is important, the backrest should stop at a level approximately 200mm below the shoulders (95th percentile male = 450mm, 5th percentile female = 305mm). It is likely that this constraint has been overemphasized in the past – perhaps from a puritanical distrust of high-backed chairs in the working environment. The higher the backrest the better supported is the trunk. Many ergonomists would now recommend a backrest of 500mm in height for office chairs (especially those used by VDU operators). The back of an easy chair should reach the level the level of the back of the head of a tall person. (Approximately equal to sitting eye height, 95th percentile male = 850mm). If the backrest is too low, a tall person will slump down in the seat in an attempt to support his head, in doing so his buttocks will move forward along the seat giving the impression that it is not sufficiently deep.

Experimental studies have shown that stress to the spine will be reduced if the seat back has a convex pad in the lumbar region. In a non-adjustable seat the centre of this convexity should be 200mm to 250mm above the seat base. A lumbar pad which is too pronounced is probably worse than none at all. (A gentle 25mm to 30mmm bulge in the lumbar region is about right.) Attempts to reflect the curve of the nape of the neck in the contours of a non-adjustable backrest are doomed to failure since this region is too variable in its location and too sharp in its curvature – a movable cushion is probably the best solution.

- Armrests

We cannot argue that an armrest which is too high is better or worse than one which is too low. An average value of male and female sitting elbow heights, 240mm above the seat, seems reasonable.

- Seat breadth (single occupant)

Seats without arms do not require to support the entire breadth of the hips but anything below about 400mm is probably too small. A clearance of 460mm between armrests will just be sufficient for a plump lady (99th percentile unclothed). Allowing some leeway, a minimum of 500mm is desirable.

Width of knee-hole clearance beneath a desk should allow for a relaxed posture of the lower limbs, a minimum of 600mm is required.

- Seat breadth (two or more occupants)

When two or more people must sit next to each other on bench style seats, shoulder breadth is the appropriate clearance dimension. When two persons sit next to each other, the probability that they will both have greater than the 95th percentile shoulders is only 1 in 400. The space required for a 95th percentile pair of people is a little less than twice the 95th percentile shoulder breadth.

Allowing 40mmm per person for outdoor clothing, two people require a clearance of 1075mm at shoulder level and three require 1595mm.

- Seat angles

For postural support a reclined sitting position is best -  to relax your muscles you must be “laid back”. Many working tasks prevent this desirable position and a ‘perpendicular’ position may be the best we can hope for. An office chair should provide for both these alternatives. In a comfortable laid-back position, the backrest makes an angle of 1050 to 1100 to the horizontal. For an easy chair this could be increased to 1200 or more – although these steeper inclinations can make it difficult for the elderly of infirm to stand up and sit down.

In inclined sitting positions, there may be a tendency for the buttocks to slide forward. This may be counteracted by tilting the seat surface backwards by 50 to 100.

- Table heights

The underside of tables should provide clearance for the thighs and knees. The correct height for the table surface depends on the task to be performed upon it. Ideally, keyboards should be at elbow height and writing surfaces about 50mm above elbow heights. Some people recommend a sloped writing surface e.g. 150 – with some means for preventing loose objects from rolling off.

Office desks are currently standardized at 720 (+/-10) mm for writing and 670 (+/-10) mm for typing.

This is a satisfactory compromise – but is too low for some tall people and some short people need a footstool. The only way around this difficulty would be to make an adjustable desk – and these are slowly coming in.

A typical dining table is about 780mm high and is used with a 470mm seat. This gives a table surface 70mm  above the average sitting elbow height – which is very reasonable, but the seat is noticeably too high for the shorter person.

BS5940 deals with the dimensions of office furniture and workstations.

BS5873 deals with school furniture.