# Anthropometrics

Anthropometrics deals with the relationships between the dimensions of the user and those of the object. These relationships are of three basic kinds:

- Clearance

- Reach

- Posture

Clearance (head room, knee room, elbow room, etc.) must be adequate to accommodate the bodily dimensions of a large-sized member of the user population. In these cases, anthropometric data allow us to specify the minimum dimension acceptable in the object. Hence the height of a table (underside) should not be less than the knee height of a 95th percentile user.

Reach dimensions, on the other hand, should be based on a small member of the population. They allow us to specify the maximum dimension allowable in the object. Hence the height of a seat should not be greater than the lower leg length of a 5th percentile user. (This particular dimension is usually called popliteal height since anatomists call the back of the knee the popliteal region.)

Postural problems are often more complicated than those of clearance and reach. For example, if we wanted to work out the height of a kitchen worktop, it is not obvious whether we should design for tall or short people. Various studies have shown that such a worktop should be between 50mm and 100mm below the elbow height of the user when standing.) We should select the worktop height which “accommodates” the greatest possible proportion of the target population. Worktop height should be 75mm below the elbow height of the average user. If the height which is chosen falls outside the desirable limits for a significant proportion of the population, we have to decide whether the problems arising from a worktop which is too high are worse than those arising from one which is too low. This might lead us to shift our planned height upward or downward in order to achieve the best possible compromise. Or we may conclude that an adjustable worktop is required.

Group A Heights of principal anatomical landmarks

- Stature

The height of the fully erect standing person. Clearance from floor to head obstacles. Stature is an important reference dimension for comparing populations.

- Eye height

The eye level of the standing person. Defines the centre of the visual field and is an important reference level for the location and design of visual displays.

- Shoulder height (Acromial)

The height of the acromion – the bony ‘point’ of the shoulder. It approximately defines the centre of rotation of the shoulder joint and may be used with dimensions 18 & 23 for calculating zones of reach.

- Elbow height

Reference level for determining the heights of working surfaces.

- Hip height (Trochanteric)

Height of the greater trochanter (a bony prominence at the top of the thigh bone). Defines the centre of rotation of the hip joint and the functional length of the lower limb. The level at which loads are commonly carried.

- Knuckle height

Reference level for hand grips. For support (handrails,etc.) a level some 100mm above knuckle height is desirable. Handholds on objects for carrying should be at less than knuckle height. Lowest acceptable level for most types of hand operated controls. Optimum height for lifting actions (an average value of 750mm is often quoted).

- Fingertip height

Lowest acceptable height for fingertip operated controls

# Group B Sitting Dimensions

8. Sitting Height

Vertical distance of the crown of the head above the seat surface. Clearance from seat to overhead obstacles for sitting person. Add 10mm for thick clothing beneath buttocks, 25mm for hat and 35mm for safety helmet.

- Sitting eye height

Eye level of the sitting person above the seat surface. Reference level for the location of visual displays. Subtract up to 40mm for sitting slump.

- Sitting shoulder height (Acromial)

Shoulder level of the sitting person above the seat surface. Subtract up to 40mm for sitting slump.

- Sitting elbow height

The height of the underside of the elbow above the seat. Suitable height for armrests in many seats. Reference level for table heights, etc, keyboards should be at elbow height, writing surfaces should be 50mm to 100mm above elbow height.

- Thigh thickness

Vertical distance from the seat surface to the higher part of the thigh. Clearance required between seat and underside of table or other obstacle. This dimension interacts strongly with elbow rest height.

- Buttock-knee length

Horizontal distance from the back of the uncompressed buttocks to the front of the knee in the standard sitting position. Clearance required between seat back and obstacles in front of the knee. Add correction for outdoor clothing.

- Buttock-popliteal length

Horizontal distance from the uncompressed buttocks to the popliteal fossa (the back of the knee) in the standard sitting position. Maximum acceptable depth of a seat.

- Knee height

Height of the top of the knee from the floor in the standard sitting position. Clearance required beneath tables, etc. Add correction for shoes.

- Popliteal height

Height of the popliteal fossa (the back of the knee) from the floor in the standard sitting position. Defines the maximum acceptable height of a seat. The optimum height of a seat is commonly quoted as 25mm to 50mm below popliteal height. Add correction for shoes.

- Shoulder breadth (Bideltoid)

Maximum breadth across the shoulders. Clearance required in upper part of work space. Add correction for outdoor clothing.

- Biacromial breadth

Horizontal distance between the acromia (the bony ‘points’ of the shoulders). Defines centre of rotation of upper limbs.

- Elbow-elbow breadth

Maximum lateral distance across the elbows while the arms hang loosely by the sides. Clearance required at elbow height. Add correction for outdoor clothing.

- Hip breadth

Maximum lateral distance across the hips. Clearance required at seat height (between the arms of chairs). A very obese person may have a hip breadth of 550mm. Add correction for outdoor clothing. The breadth of a seat which does not have arms, may comfortably be 50mm less than hip breadth.

|  |  | Men | Women |
| --- | --- | --- | --- |
|  |  | 5th %le | 50th %le | 95th %le | 5th %le | 50th %le | 95th %le |
|  | British Adults 19 - 65 years |  |  |  |  |  |  |
|  | Body weight (kg) | 55 | 75 | 95 | 45 | 63 | 81 |
| 1 | Stature | 1625 | 1740 | 1855 | 1510 | 1610 | 1710 |
| 2 | Eye Height | 1515 | 1630 | 1745 | 1405 | 1505 | 1605 |
| 3 | Shoulder Height | 1315 | 1425 | 1535 | 1215 | 1310 | 1405 |
| 4 | Elbow Height | 1005 | 1090 | 1175 | 930 | 1005 | 1080 |
| 5 | Hip Height | 840 | 920 | 1000 | 740 | 810 | 880 |
| 6 | Knuckle Height | 690 | 755 | 820 | 660 | 720 | 780 |
| 7 | Fingertip Height | 590 | 655 | 720 | 560 | 625 | 690 |
| 8 | Sitting Height | 850 | 910 | 970 | 790 | 850 | 910 |
| 9 | Sitting Eye Height | 730 | 790 | 850 | 685 | 740 | 795 |
| 10 | Sitting Shoulder Height | 540 | 595 | 650 | 505 | 555 | 605 |
| 11 | Sitting Elbow Height | 195 | 245 | 295 | 185 | 235 | 285 |
| 12 | Thigh Thickness | 135 | 160 | 185 | 125 | 155 | 185 |
| 13 | Buttock-Knee Length | 545 | 595 | 645 | 520 | 570 | 620 |
| 14 | Buttock-Popliteal Length | 440 | 495 | 550 | 435 | 480 | 530 |
| 15 | Knee Height | 495 | 545 | 595 | 455 | 500 | 545 |
| 16 | Popliteal Height | 390 | 440 | 490 | 355 | 400 | 495 |
| 17 | Shoulder Breadth (bideltoid) | 420 | 465 | 510 | 355 | 395 | 435 |
| 18 | Biacromial breadth | 365 | 400 | 435 | 325 | 355 | 385 |
| 19 | Elbow-Elbow Breadth | 370 | 450 | 530 | 320 | 385 | 450 |
| 20 | Hip Breadth | 310 | 360 | 410 | 305 | 370 | 435 |
| 21 | Chest (Bust) depth | 215 | 250 | 285 | 205 | 250 | 295 |
| 22 | Abdominal depth | 220 | 270 | 320 | 205 | 255 | 305 |
| 23 | Shoulder-Fingertip Length | 720 | 780 | 840 | 650 | 705 | 760 |
| 24 | Shoulder-Elbow Length | 330 | 365 | 400 | 300 | 330 | 360 |
| 25 | Elbow-Fingertip Length | 440 | 475 | 510 | 400 | 430 | 460 |
| 26 | Span | 1655 | 1790 | 1925 | 1490 | 1605 | 1720 |
| 27 | Elbow Span | 870 | 945 | 1020 | 780 | 850 | 920 |
| 28 | Standing Overhead Reach | 2040 | 2170 | 2300 | 1895 | 2010 | 2125 |
| 29 | Sitting Overhead Reach | 1255 | 1355 | 1455 | 1150 | 1255 | 1340 |
| 30 | Forward Reach | 835 | 890 | 945 | 760 | 810 | 860 |
| 31 | Hand Length | 173 | 189 | 205 | 159 | 174 | 189 |
| 32 | Hand Breadth (Metacarpal) | 79 | 87 | 95 | 69 | 76 | 83 |
| 33 | Hand Breadth (including thumb) | 97 | 105 | 113 | 84 | 92 | 100 |
| 34 | Palm Length | 97 | 107 | 117 | 89 | 97 | 105 |
| 35 | Index Finger Length | 64 | 72 | 80 | 60 | 67 | 74 |
| 36 | Index Finger Breadth | 18 | 21 | 24 | 15 | 18 | 21 |
| 37 | Thumb Breadth | 20 | 23 | 26 | 16 | 19 | 22 |
| 38 | Hand Thickness at Palm | 28 | 33 | 38 | 23 | 28 | 33 |
| 39 | Hand Thickness (including thumb) | 44 | 51 | 58 | 40 | 45 | 50 |
| 40 | Maximum grip diameter | 45 | 52 | 59 | 43 | 48 | 53 |

|  |  | Boys | Girls |
| --- | --- | --- | --- |
|  |  | 5th %le | 50th %le | 95th %le | 5th %le | 50th %le | 95th %le |
|  | 15-18 years |  |  |  |  |  |  |
| 1 | Stature | 1610 | 1735 | 1855 | 1520 | 1620 | 1715 |
| 2 | Eye Height | 1490 | 1615 | 1740 | 1410 | 1510 | 1610 |
| 3 | Shoulder Height | 1310 | 1420 | 1530 | 1225 | 1315 | 1405 |
| 4 | Elbow Height | 995 | 1080 | 1170 | 930 | 1005 | 1080 |
| 5 | Hip Height | 835 | 915 | 995 | 750 | 820 | 885 |
| 6 | Knuckle Height | 675 | 745 | 815 | 665 | 720 | 780 |
| 7 | Fingertip Height | 555 | 625 | 695 | 550 | 610 | 665 |
| 8 | Sitting Height | 825 | 900 | 970 | 800 | 855 | 905 |
| 9 | Sitting Eye Height | 715 | 785 | 850 | 690 | 740 | 790 |
| 10 | Sitting Shoulder Height | 520 | 580 | 635 | 500 | 550 | 595 |
| 11 | Sitting Elbow Height | 185 | 235 | 285 | 185 | 230 | 270 |
| 12 | Thigh Thickness | 125 | 150 | 180 | 120 | 145 | 170 |
| 13 | Buttock-Knee Length | 530 | 580 | 630 | 510 | 555 | 600 |
| 14 | Buttock-Popliteal Length | 440 | 490 | 545 | 435 | 480 | 520 |
| 15 | Knee Height | 500 | 545 | 590 | 455 | 500 | 540 |
| 16 | Popliteal Height | 395 | 440 | 485 | 360 | 405 | 445 |
| 17 | Shoulder Breadth (bideltoid) | 385 | 435 | 490 | 360 | 395 | 430 |
| 18 | Biacromal breadth | 345 | 385 | 420 | 330 | 355 | 385 |
| 19 | Elbow-Elbow Breadth |  |  |  |  |  |  |
| 20 | Hip Breadth | 290 | 330 | 375 | 300 | 345 | 385 |
| 21 | Chest depth | 170 | 220 | 265 | 185 | 225 | 265 |
| 22 | Abdominal depth | 190 | 230 | 270 | 185 | 220 | 255 |
| 23 | Shoulder-Fingertip Length | 715 | 780 | 845 | 650 | 700 | 750 |
| 25 | Elbow-Fingertip Length | 435 | 470 | 510 | 395 | 425 | 455 |
| 26 | Span | 1630 | 1785 | 1935 | 1505 | 1610 | 1720 |
| 27 | Elbow Span | 855 | 940 | 1025 | 785 | 850 | 915 |
| 28 | Standing Overhead Reach | 1955 | 2110 | 2260 | 1825 | 1965 | 2110 |
| 29 | Sitting Overhead Reach | 1120 | 1225 | 1330 | 1035 | 1135 | 1235 |
| 30 | Forward Reach | 650 | 725 | 795 | 605 | 670 | 730 |
| 31 | Hand Length | 170 | 190 | 205 | 160 | 175 | 190 |
| 32 | Hand Breadth (Metacarpal) | 80 | 90 | 95 | 70 | 75 | 80 |
| 41 | Foot Length | 240 | 265 | 285 | 220 | 240 | 260 |
| 42 | Foot Breadth | 90 | 100 | 110 | 80 | 90 | 100 |
| 47 | Head Length | 185 | 200 | 210 | 170 | 180 | 190 |
| 48 | Head Breadth | 145 | 155 | 165 | 135 | 145 | 155 |

|  |  | Boys | Girls |
| --- | --- | --- | --- |
|  |  | 5th %le | 50th %le | 95th %le | 5th %le | 50th %le | 95th %le |
|  | 9-14 years |  |  |  |  |  |  |
| 1 | Stature | 1225 | 1475 | 1725 | 1210 | 1445 | 1680 |
| 2 | Eye Height | 1070 | 1340 | 1610 | 1095 | 1330 | 1565 |
| 3 | Shoulder Height | 960 | 1190 | 1420 | 950 | 1165 | 1380 |
| 4 | Elbow Height | 735 | 910 | 1085 | 725 | 895 | 1065 |
| 5 | Hip Height | 620 | 775 | 930 | 610 | 745 | 880 |
| 6 | Knuckle Height | 500 | 625 | 750 | 520 | 640 | 760 |
| 7 | Fingertip Height | 415 | 525 | 635 | 420 | 535 | 650 |
| 8 | Sitting Height | 645 | 765 | 885 | 650 | 765 | 880 |
| 9 | Sitting Eye Height | 535 | 655 | 775 | 540 | 665 | 770 |
| 10 | Sitting Shoulder Height | 395 | 480 | 585 | 380 | 475 | 570 |
| 11 | Sitting Elbow Height | 150 | 205 | 260 | 145 | 205 | 265 |
| 12 | Thigh Thickness | 95 | 130 | 165 | 90 | 125 | 160 |
| 13 | Buttock-Knee Length | 390 | 490 | 590 | 390 | 485 | 580 |
| 14 | Buttock-Popliteal Length | 315 | 405 | 495 | 330 | 410 | 490 |
| 15 | Knee Height | 370 | 465 | 560 | 370 | 450 | 530 |
| 16 | Popliteal Height | 300 | 375 | 450 | 300 | 365 | 430 |
| 17 | Shoulder Breadth (bideltoid) | 280 | 355 | 430 | 275 | 350 | 425 |
| 18 | Biacromal breadth | 270 | 325 | 380 | 260 | 215 | 370 |
| 19 | Elbow-Elbow Breadth |  |  |  |  |  |  |
| 20 | Hip Breadth | 200 | 285 | 340 | 210 | 290 | 370 |
| 21 | Chest depth | 120 | 175 | 230 | 110 | 180 | 250 |
| 22 | Abdominal depth | 145 | 195 | 245 | 145 | 195 | 245 |
| 23 | Shoulder-Fingertip Length | 520 | 645 | 770 | 500 | 625 | 750 |
| 25 | Elbow-Fingertip Length | 320 | 395 | 470 | 310 | 380 | 450 |
| 26 | Span | 1200 | 1495 | 1790 | 1170 | 1435 | 1700 |
| 27 | Elbow Span | 630 | 790 | 950 | 610 | 760 | 910 |
| 28 | Standing Overhead Reach | 1460 | 1785 | 2110 | 1440 | 1755 | 2070 |
| 29 | Sitting Overhead Reach | 830 | 1025 | 1220 | 810 | 1010 | 1210 |
| 30 | Forward Reach | 495 | 615 | 735 | 490 | 600 | 710 |
| 31 | Hand Length | 130 | 160 | 190 | 130 | 155 | 180 |
| 32 | Hand Breadth (Metacarpal) | 60 | 75 | 90 | 60 | 70 | 80 |
| 41 | Foot Length | 185 | 230 | 275 | 185 | 220 | 255 |
| 42 | Foot Breadth | 75 | 90 | 105 | 70 | 85 | 100 |
| 47 | Head Length | 165 | 185 | 205 | 155 | 175 | 195 |
| 48 | Head Breadth | 135 | 150 | 165 | 125 | 140 | 155 |