Our Lady’s High School

N5 Physics

Electricity & Properties of Matter

Problems

Data Sheet

| Speed of light in materials |  | Speed of sound in materials |
| --- | --- | --- |
| Material | Speed in ms-1 |  | Material | Speed in ms-1 |
| Air | 3 x 108 |  | Aluminium | 5 200 |
| Carbon Dioxide dioxide | 3 x 108 |  | Air | 340 |
| Diamond | 1(2 x 108 |  | Bone | 4 100 |
| Glass | 2(0 x 108 |  | Carbon dioxide | 270 |
| Glycerol | 2.1 x 108 |  | Glycerol | 1 900 |
| Water | 2(3 x 108 |  | Muscle | 1 600 |
|  |  |  | Steel | 5 200 |
| Gravitational field strengths |  | Tissue | 1 500 |
|  | Gravitational field strength on the surface in N kg-1 |  | Water | 1 500 |
| Earth | 9.8 |  | Specific heat capacity of materials |
| Jupiter | 23 |  | Material | Specific heat capacity in Jkg- oC-1 |
| Mars | 3.7 |  |  |  |
| Mercury | 3.7 |  | Alcohol | 2 350 |
| Moon | 1(6 |  | Aluminium | 902 |
| Neptune | 11 |  | Copper | 386 |
| Saturn | 9 |  | Glass | 500 |
| Sun | 270 |  | Ice | 2 100 |
| Venus | 8.9 |  | Iron | 480 |
| Uranus | 8(7 |  | Lead | 128 |
|  |  |  | Oil | 2 130 |
|  | Water | 4 180 |
| Specific latent heat of fusion of materials |  |  |
| Material | Specific latent heat of fusion in Jkg-1 |  | Melting and boiling points of materials |
|  |  |  | Material | Melting point in oC | Boiling point in oC |
| Alcohol | 0(99 x 105 |  |  |  |  |
| Aluminium | 3(95 x 105 |  | Alcohol | -98 | 65 |
| Carbon dioxide | 1(80 x 105 |  | Aluminium | 660 | 2470 |
| Copper | 2(05 x 105 |  | Copper | 1 077 | 2 567 |
| Iron | 2.67 x 105 |  | Glycerol | 18 | 290 |
| Lead | 0(25 x 105 |  | Lead | 328 | 1 737 |
| Water | 3(34 x 105 |  | Iron | 1537 | 2 737 |
|  |  | Radiation Weighting Factors |
| Specific latent heat of vaporisation of materials |  | Type of Radiation G | Radiation Weighting Factor |
| ¦Material | Sp.l.ht vap(Jkg-1) |  |  |  |
| Alcohol | 11(2 x 105 |  | alpha G | 20 |
| Carbon dioxide | 3(77 x 105 |  | beta M | 1 |
| Glycerol | 8(30 x 105 |  | fast neutrons k | 10 |
| Turpentine | 2(90 x 105 |  | gamma m | 1 |
| Water | 22(6 x 105 |  | slow neutrons ( | 3 |

1.  Current and Electrical Charge

In this section you can use the equation:

also written as

where		Q  = charge in coulombs (C)

I   = current in amperes (A)

t   = time in seconds (s).

1.	Find the missing values in the following table.

|  | Charge (C) | Current (A) | Time (s) |
| --- | --- | --- | --- |
| (a) |  | 5 | 30 |
| (b) |  | 0·005 | 3 600 |
| (c) | 3 | 1·5 |  |
| (d) | 27·6 | 2·3 |  |
| (e) | 1 800 |  | 60 |
| (f) | 94 |  | 10 |

2.	A bulb draws a current of 1 A. How much charge flows through it in 60 seconds?

3.	756 C of charge flow though an electric heater in 180 seconds. What is the current in the heater?

4.	A hairdryer operates with a current of 5 A. How much time would it take for 6 000 C to pass through the hairdryer?

| 5. | A current of 2·1 A flows through an electric shaver for 5 minutes. How much charge flows in this time? |
| --- | --- |

6.	A 60 W bulb is switched on for 30 minutes. If 450 C pass through it in this time, what is the current flowing in the bulb?

7.	A ‘surround sound’ speaker system on a TV draws a current of 0·6 A. In an average day 6 480 C of charge flows through the speaker system. For how long is the TV switched on each day?

8.	An electric kettle has a label on it as shown below.

| MODEL No. 5510 - 01 capacity 1·7 litres 9·2 A /220 - 240 V 2·2 kW |  |
| --- | --- |

After the kettle is switched on it automatically switches off when the water in it has boiled. On one occasion 1 656 C passed through the kettle before it switched off. Use the information given to work out how long the water took to boil?

9.	An electric fire is rated at 2·875 kW, 230 V, 12·5 A. How much charge will flow through this fire in a period of 2 hours 20 minutes?

10.	One day an electric iron was switched on from 1·45 p.m. until 3·15 p.m. What current was drawn by the iron if 2·484 x 104 C passed through it in this time?

2.  Electric Fields and Potential Difference

1.	Copy the following charge arrangements and sketch the corresponding electric field 	patterns:

(a)	a positive point charge

(b)	a negative point charge

(c)	a pair of point charges with opposite charge

(d)	a pair of parallel plates with opposite charge

2.	Which of the following will experience a force when placed in an electric field.

There may be more than one correct answer here.

A	alpha radiation

B	atoms

C	beta radiation

D	charged particles

E	gamma radiation

3.	For each of the following electric fields, state the potential difference across the field.

(a)						(b)

(c)						(d)

4.	In each of the following circuits, the “potential” at various points is shown. For each 	circuit, determine the “potential difference” between points X and Y.

(a)						(b)

(c)						(d)

5.	Which of the following statements correctly explains what is meant by a “12 V 	supply”.

A 	12 volts are supplied to each coulomb of charge.

B	12 joules of energy are supplied to each coulomb of charge.

C	12 joules of energy are supplied each second.

D	12 coulombs of charge pass through each second.

E	12 coulombs of charge are supplied to each joule of energy.

3.  AC and DC

1.	D.C. stands for Direct Current. Explain what is meant by this in terms of the size and 	direction of the electric current.

2.	A.C. stands for Alternating Current. Explain what is meant by this in terms of the size 	and direction of the electric current.

3.	State the size and frequency of the mains voltage.

4.	For each of the following, state whether d.c. or a.c. is produced.

(a)	the mains electricity supply

(b)	a car battery

(c)

(d)

5.	(Extension question)

Voltage can be measured using an oscilloscope by multiplying the “volts per division” 	setting by the number of divisions (or boxes) between the signal and the centre “zero” 	line on the oscilloscope grid. For an a.c. signal, the “peak voltage” is the maximum 	voltage reached in any cycle.

For each of the following signals, determine the d.c. voltage or the a.c. peak voltage 	shown. The “volts per division” setting is given in each case.

(a)				   (b)			   	 (c)

3 volts per division		       1.5 volts per division            0.5 volts per division

4.  Basic Electrical Components

1.	Find out and draw the symbol for each of the following electrical and electronic 	components:

(a)	lamp

(b)	connecting lead

(c)	battery

(d)	cell

(e)	motor

(f)	resistor

(g)	switch

(h)	variable resistor

(i)	voltmeter

(j)	ammeter

(k)	fuse

(l)	buzzer

(m)	bell

2.	Draw a circuit consisting of one lamp, one switch, one battery and one buzzer 	connected in series.

3.	Draw a circuit that will allow 3 bulbs to be switched on and off separately. Each bulb 	will require its own switch. The circuit should operate from 2 batteries connected 	in 	series.

5.  Measuring Current, Voltage and Resistance

1.	A student sets up a circuit, as shown below, in order to switch on a lamp.

The student wants to measure the voltage across the lamp and the current through it.

(a)	What should the student use in order to measure the voltage across the lamp?

(b)	What should be used to measure the current in the lamp?

(c)	Redraw the circuit to show the correct positions of these meters.

(d)	Draw a circuit to show how the student could measure the resistance of the 		lamp directly.

2.	The following circuit is set up to investigate the effect of resistance on current.

(a)	Describe what happens to the ammeter reading as the resistance of the variable 		resistor is increased.

(b)	Present the results in the following table as a line graph:

| Resistance () | 100 | 200 | 300 | 400 | 500 |
| --- | --- | --- | --- | --- | --- |
| Current (A) | 0.120 | 0.060 | 0.040 | 0.030 | 0.025 |

3.	The resistance of the variable resistor, in the circuit below, is decreased.

Describe and explain what happens to the brightness of the lamp as the resistance 	decreases.

6.  Current and Voltage in Series Circuits

Helpful Hint

The rules for series circuits are:

1.	the current is the same at all points in the circuit

2.	the voltage of the source is shared amongst the components in the circuit.

1.	Two identical 2·5 V bulbs are connected to a supply as shown. Determine the voltage of the supply.

2.	Four identical resistors are connected across a 12 V supply as shown in the diagram. Determine the voltage across each of the resistors.

3.	A simple circuit with a bulb and resistor in series is shown below.

(a)	The bulb is operating at its correct voltage and power rating. Determine the 		voltage across resistor R.

(b)	The current in the bulb is 3 A. Determine the current flowing in the resistor.

4.     Two resistors are connected in series to a supply as shown in the diagram.

(a)		The current in the 200 ( resistor is 0·05 A. Determine the current in the other 		resistor.

(b)		The voltage across the 100 ( resistor is 5 V. Determine the voltage across the

200 ( resistor.

5.     A rheostat is used as a dimmer switch in a simple series circuit as shown.

The rheostat is adjusted until the bulb is shining brightly. The voltage across the bulb is 13·8 V and the current through the rheostat at this setting is 1·7 A.

(a)	Calculate the voltage across the rheostat.

(b)	Determine the current flowing in the bulb.

7.  Current and Voltage in Parallel Circuits

Helpful Hint

The rules for parallel circuits are:

1.	the voltage is the same across all the components in parallel.

2.	the current from the supply is shared amongst the different branches

of the circuit.

1.	Two resistors are connected in parallel to a 12 V battery.

(a)	Determine the voltage across R1.

(b)	Determine the voltage across R2.

(c)	Calculate the current drawn from

the battery.

2.	Two identical bulbs and a resistor are connected

in parallel to a 6 V supply.

(a)	Determine the voltage across L2 .

(b)	A current of 1·8 A flows through each of the bulbs.

Calculate the current flowing through the resistor.

3.	An electric fire has three elements which can be switched on and off independently. The elements are connected in parallel to the mains supply. Each element draws a current of 0·3 A when switched on.

(a)	Determine the voltage across the middle

element.

(b)	Calculate the total current flowing from the

supply when two of the elements are switched 	on.

(c)	Calculate the maximum current drawn

from the mains by the fire.

4.	The headlamps and side lights in a car are connected in parallel. The diagram below shows how they are connected. The side lights (L1 & L2) may be switched on by themselves using switch S1. The headlights (H1 & H2) are switched on by switch S2 and only come on if the sidelights are already on.

(a)	Determine the voltage across the sidelight L1.

(b)	Determine the voltage across the headlight H2.

(c)	Each sidelight draws a current of 3 A from the car battery. Calculate the total

current drawn from the battery when S1 only is closed.

(d)	Each headlight draws a current of 5 A from the car battery. Calculate the total 		current drawn from the battery when S1 and S2 are closed.

5.	A hairdryer contains a motor and heating elements (resistors). The hairdryer shown below has three heat settings- cold, warm and hot. The circuit diagram shows how these settings are achieved using switches A, B and C.

The motor draws a current of 3 A from the mains and the heating elements draw a current of 2 A each from the mains.

(a)	State which switches must be closed to make the hairdryer blow warm air.

(b)	Calculate the current drawn from the mains when the hairdryer blows warm

Air.

(c)	State which switches must be closed to make the hairdryer blow hot air.

(d)	Calculate the current drawn from the mains when the hairdryer blows hot air.

(e)	Determine the minimum current drawn when the hairdryer is on.

(f)	Determine the voltage across the motor.

8.  Circuit Applications

1.	Junior Spark tries his hand at some DIY electrics in and around his new home.

He designs two circuits. Circuit 1 is a model for a room light and Circuit 2 is a model 	for toy car lights.

His designs are shown below.

Sidelights 12 V , 24 W			Headlights 12 V , 36 W

Look at the circuits and answer the following questions.

(a)	Describe the function of the variable resistor in circuit 1.

(b)	In circuit 2, which switches must be closed to switch on the head lights?

(c)	What is the advantage of having the sidelights and the headlights connected in 		parallel instead of in series with one another?

2.	Give 2 examples from a typical house where 2 switches are connected in series to 	operate an electrical device.

3.	Does household wiring connect ceiling lights in series or in parallel?

4.	Why do modern houses have circuit breakers instead of fuses?

5.	(Homework task!) Find out what the various circuits are in your own household 	wiring. You can do this by checking your “fuse box” which will usually have each 	circuit labelled.

9.  Ohm’s Law

In this section you can use the equation:

also written as:

where		V = voltage in volts (V)

I = current in amps (A)

Helpful Hint.

Many appliances run from mains voltage which is 230 V ac.

Useful units for electricity are:

1 (A = 0·000 001 A = 1 x 10-6 A

1 mA = 0·001 A = 1 x 10-3 A

R = resistance in ohms (().

1.	Find the missing values in the following table.

|  | Voltage (V) | Current (A) | Resistance (() |
| --- | --- | --- | --- |
| (a) |  | 15 | 35 |
| (b) |  | 0·2 | 1 000 |
| (c) | 230 |  | 125 |
| (d) | 24 |  | 550 |
| (e) | 120 | 12 |  |
| (f) | 6 | 6·25 x 10-3 |  |

2.	Look at the following circuits and calculate the supply voltage in each case:

(a)			    (b)				(c)

3.	Look at the following circuits and calculate the current in each case:

(a)   24 V		    (b)	    12 V			(c)         48 V

4.	Look at the following circuits and calculate the unknown resistance in each case:

(a)	24 V		(b)	     12 V		(c)        48 V

5.	Calculate the resistance of a lamp if the current through it is 10 mA when operated by a 24 V supply.

| 6. A power drill is operated at mains voltage and has a resistance of 1·5 k(. Calculate the current through the drill. |  |
| --- | --- |

7.	The maximum current an electric motor can safely handle is 10 mA and it has a resistance of 360 (. Calculate its safe operating voltage.

8.	A cooker draws a maximum current of 28·75 A and has a resistance of 8 (. At what voltage should it operate?

9.	Hairdryers work from the mains voltage and can have currents of up to 15 mA flowing through them. Calculate the resistance of the hairdryer.

10.	Overhead cables have resistance of 25 k(. If the voltage across the cables is 4 000 V calculate the current through them.

10.  Resistance in Series

In this section you can use the equation:

where	Rs = total resistance of a series circuit or series section of a circuit ().

1.	Three resistors R1, R2 and R3 are arranged in series as shown in the diagram below.

Find the missing values in the table.

|  | R1 (() | R2 (() | R3 (() | Rs (() |
| --- | --- | --- | --- | --- |
| (a) | 5 000 | 490 | 85 |  |
| (b) | 80 | 300 | 25 |  |
| (c) | 800 | 2 000 | 200 |  |
| (d) | 700 | 300 |  | 1 400 |
| (e) |  | 140 | 100 | 550 |
| (f) | 225 |  | 85 | 390 |

2.	Calculate the total resistance of the following circuit.

3.	The resistance of the following circuit is 8·8 k. Calculate the resistance of  R.

11.  Resistance in Parallel

National 5

In this section you can use the equation

1 1 1 1 Rp R1 R2 R3

where	Rp = total resistance of a parallel circuit or parallel section of a circuit ().

1.	Calculate the total resistance of each of the following circuits:

(a)				(b)				(c)

(d)				(e)				(f)

(g)				(h)				(i)

2.	Calculate the total resistance of each of the following circuits:

(a)				(b)				(c)

(d)				(e)				(f)

3.	The total resistance of the circuit below is 80 . Calculate the resistance of  R.

4.	The total resistance of the following circuit is 112·5 . Calculate the resistance of resistor A.

5.	The total resistance of the following circuit is 240 . Calculate the resistance of resistor X

## Combination Circuits

6.	Calculate the total resistance in each of the following networks:

(a)						(b)

(c)						(d)

(e)						(f)

7.	The following circuit shows part of a car lighting system.

Calculate the resistance between points:

(a)	X and Y

(b)	Y and Z

(c)	X and Z.

8.	Calculate the resistance of the network of resistors shown below.

9.	Which network of resistors has the lowest total resistance?

Network A				      Network B

10.	A school technician has different resistors to use in building house wiring models.

He has two 10 ( resistors, two 50 ( resistors and two 100 ( resistors.

How can these resistors be combined to produce a total resistance of:

(a)	260 (		(b)	300 (		(c)	30 (		(d)	35 (?

12.  Resistance & Ohm’s Law Exam Style Question

- A student investigates the resistance of a resistor using the circuit shown.

(a) Copy and complete the circuit diagram to show where a voltmeter must be connected to measure the voltage across resistor R.

(b) Describe how the student obtains a range of values of voltage and current.

(c) The results of the student’s investigation are shown.

Use all these results to determine the resistance of resistor R.

(d) Draw a graph of the student’s results.

(e) The student now replaces resistor R with a filament lamp and repeats the investigation. A sketch graph of the student’s results is shown.

State a conclusion that can be made about the resistance of the filament lamp.

13.  Electrical Power

Power, Energy and Time

In this section you can use the equation:

also written as

where		P = power in watts (W)

E = energy in joules (J)

t = time in seconds (s).

1.	Find the missing values in the following table.

|  | Power (W) | Energy (J) | Time (s) |
| --- | --- | --- | --- |
| (a) |  | 1 500 | 30 |
| (b) |  | 180 000 | 36 000 |
| (c) | 100 |  | 600 |
| (d) | 1 200 |  | 2 |
| (e) | 3 000 | 120 000 |  |
| (f) | 2·5 | 25 |  |

2.	How long will it take for a 60 W bulb to use 720 J of electrical energy?

| 3. A bulb uses 45 000 J of energy in 300 seconds. What is its power rating? |  |
| --- | --- |

4.	    	A 50 W immersion heater is switched on for 80 seconds. How much electrical energy

passes through it in this time?

| 5. | Calculate the power rating of an electric sewing machine which uses 4 560 J of energy in 8 minutes. |
| --- | --- |

6.	A 1 200 W hairdryer is switched on for 20 minutes. How much electrical energy does it use?

7.	For how many minutes must a 600 W shaver be switched on in order to use 540 000 J of electrical energy?

8.	An electric fire uses 5·22 MJ of electrical energy in half an hour. Calculate the power rating of the fire.(1 MJ = 1 x 106 J = 1 000 000 J )

9.    How long will it take a 1·4 kW paint stripper to use 1·68 MJ of electrical energy?

10.	A microwave oven is on for twenty minutes each day. If it uses 7·98 MJ of electrical energy in one week, what is its power rating?

## Power, Current and Voltage

In this section you can use the equation:

also written as

where:		P = power in watts (W)

I  = current in amps (A)

V = voltage in volts (V).

Helpful Hint

The voltage of the mains is 230 V ac.

1.	Find the missing values in the following table.

|  | Power (W) | Current (A) | Voltage (V) |
| --- | --- | --- | --- |
| (a) |  | 2·5 | 12 |
| (b) |  | 0·6 | 9 |
| (c) | 1·5 x 103 |  | 230 |
| (d) | 36 |  | 12 |
| (e) | 0·624 | 2·6 x 10-3 |  |
| (f) | 1·5 | 0·25 |  |

2.	A car battery supplies a voltage of 12 V. One headlamp bulb draws a current of 3 A. What is the power rating of this bulb?

| 3. | An electric shower has a power rating of 12 W and draws a current of 0·11 A. What voltage is required to operate the shower? |
| --- | --- |

4.	What current flows through a 230 V, 60 W household lamp when it is operating at the correct voltage?

5.	Calculate the power rating of an electric drill which draws a current of 3 A when connected to the mains.

6.	What would be the reading on the ammeter in the circuit shown?

7.	The following information was found on the rating plate of a food processor:

Calculate the current flowing in the food processor.

8.	A fridge has a power rating of 160 W. When it is plugged into the mains what current will it draw?

9.	A radio has a power rating of 6 W and draws a current of 0·5 A when operating normally.

(a)	What voltage does this radio require?

(b)	How many 1·5 V batteries would be needed to operate the radio?

10.	The circuit shows a 1 kW heating element operating correctly.

What is the voltage of the supply?

11.	A torch bulb draws a current of 500 mA. It has a power rating of 1·75 W. What voltage is required to light the bulb to its correct brightness?

12.	An electric locomotive on the East Coast line gets its electricity from the overhead cables which supply 25 kV a.c. The locomotive has a top speed of 140 mph and it operates at 4·7 MW. Calculate the current flowing to the locomotive.

13.	 A helium - neon laser emits red light and has many uses in medicine. The laser uses the 230 V mains supply and has a power rating of 5 mW. What current flows in the laser?

14.	The current flowing in an electric keyboard is measured as 800 mA. What voltage is required to operate the keyboard if it has a power rating of 7·2 W?

15.	An electric fire has three heating elements which can be switched on and off independently. Each element has a power of 1·3 kW and is controlled by a switch on the side of the fire.

(a)	Calculate the current drawn from the socket when one heating element is

switched on.

(b)	What is the maximum current that the fire could draw?

## Power and Resistance

Helpful Hint By combining the formulae: we have alternative forms of the formula for power. i.e. P = I (IR) and P = (V/R) V P = I 2 R P = V2/R

| 1. | Calculate the power rating of a lawn mower which has a resistance of 70·5 ( and draws a current of 2·5 amps. |
| --- | --- |

2.	What power is dissipated in the element of a toaster if it has a resistance of 64 ( and draws a current of 3·75 amps?

3.	Find the power rating of a television given that it operates at mains voltage and has a resistance of 480 (.

4.	What would be the power rating of an iron if it operates at mains voltage and has a resistance of 45 (?

5.	Calculate the power rating of a hedge trimmer given that it draws a current of 1·67 A and has a resistance of 144 (.

6.	Calculate the power rating of a Karaoke machine if it has a resistance of 5 760 ( and operates at mains voltage.

7.	How much power is dissipated in curling tongs if they draw a current of 1·05 A and have a resistance of 230 ( while operating from the mains?

8.	A microwave oven has a resistance of 68 ( and works properly from a mains supply. What is the power rating for such an oven?

|  | Find the power rating of a Hoover designed with a resistance of 110 ( when operating at mains voltage. |
| --- | --- |

9.

10.	What current is drawn from the supply by a transistor radio if it has a power rating of

3 W and a resistance of 12 (?

11.	Find the resistance of a table lamp which has a power rating of 115 W and draws a current of 0·5 A.

12.	An alarm clock is driven by a domestic supply voltage of 230 V. What is its resistance if it has a power rating of 2 W?

13.	Calculate the total resistance of an electric fire if it operates safely at 230 V and uses electrical energy at a rate of 750 W.

14.	Calculate the voltage of a car alarm which has a power rating of 3 W and resistance of 50 (.

| 15. Find the power rating of an electric food mixer if it operates at mains voltage and has a resistance of 400 (. |  |
| --- | --- |

## 14.  Miscellaneous Questions on Circuits

1.	The following circuit is set up in a laboratory.

The bulb is switched on for 3 minutes and the voltmeter and ammeter readings remain as shown in the diagram.

(a)	Calculate the power rating of the bulb.

(b)	Calculate the resistance of the bulb.

(c)	Calculate how much electrical energy is supplied to the bulb in the 3 minutes.

(d)	Calculate how much charge passes through the bulb in the 3 minutes.

2.	The resistor in the following circuit has a power rating of 0·09 W.

(a)	What reading would you expect to find on the ammeter?

(b)	What reading would you expect to find on the voltmeter?

(c)	How long would it take for 5·4 joules of electrical energy to be supplied to the 		resistor?

(d)	How much charge passes through the resistor in 1 minute?

3.	Some students decide to measure the resistance of a torch bulb and each set up a circuit to do this. The circuits are shown below.

(a)	Which circuit has been set up correctly? Explain your answer.

(b)	Use the following results to plot a graph of voltage against current and

hence or otherwise find the resistance of the torch bulb.

| Current (A) | Voltage (V) |
| --- | --- |
| 0·5 | 5 |
| 0·8 | 8 |
| 1·1 | 11 |
| 1·4 | 14 |
| 1·7 | 17 |

4.	The rating plate on an electric kettle is shown below.

(a)	Calculate the current flowing in the kettle.

(b)	What is the resistance of the heating element in the kettle?

5.	A vacuum cleaner connected to the mains draws a current of 3·1 A.

(a)	What is the power rating of the vacuum cleaner?

(b)	What is the resistance of this appliance?

6.	An iron rated at 1(1 kW draws a current of 4·6 A. One day 8 280 C of charge passed through the iron.

(a)	How long was the iron in use?

(b)	How much electrical energy was supplied in this time?

7.	A bulb in a laboratory operates with a current of 2 A. During an experiment 1 200 C of charge flow through the bulb, supplying it with 14 400 J of electrical energy.

(a)	How long did this experiment last?

(b)	What was the power rating of the bulb?

8.	The power rating of an electric fire is 3 kW and it draws a current of 12·5 A. One afternoon the fire used up 8·1 MJ of electrical energy.

(a)	For how long was the fire switched on?

(b)	How much charge passed through the fire in this time?

9.	An electrical appliance has a power rating of 2·4 kW. If 432 000 J of electrical energy are supplied to the appliance by 1 800 C of charge, calculate the current drawn by the appliance.

10.	The following label is attached to a hairdryer.

Type 4533

1·44 kW

230 V / 6 A

Calculate the amount of electrical energy supplied to the hairdryer by 4 320 C of 	charge.

11.	Bulbs B1, B2 and B3 are all identical. What is the voltage across bulb B2 and bulb B3?

12.	Look at the circuit shown and find:

(a)	the voltage across R2

(b)	the current through R1.

13.	In the following circuit the bulbs are identical. Find:

(a)	the voltage across each bulb

(b)	the current through each bulb.

14.	In the following circuit all the resistors are identical. Find:

(a)	the voltage across each resistor

(b)	the current through each resistor.

15.	Daral has a selection of resistors and has to combine them in some way to obtain a total resistance of 60 (.

He has two 5 (, two 20 ( and two 90 ( resistors.

He sets up three different networks as shown below. Which one is correct?

Network 2

Network 3

15.  Energy Transformations

In this section you can use the following equations:

E  =  P t

Ep  =  m g h

P  =  I  V

where	E	=	energy in joules (J)

I	=	current in amps (A)

t	=	time in seconds (s)

Ep	=	gravitational potential energy in joules (J)

m	=	mass in kilograms (kg)

g	=	gravitational field strength in newtons per kilogram (Nkg-1)

h	=	height in metres (m)

P	=	power in watts (W)

V	=	voltage in volts (V)

Helpful Hint

Energy cannot be created or destroyed only changed from one form to another. In a pumped storage hydroelectric power station, the potential energy of the water is converted to electrical energy when the water falls from the reservoir into the turbines attached to the generator. At night when the water is pumped back up to the reservoir electrical energy in the pump is converted into potential energy.

Day time									Night time

potential energy	       electrical energy	      electrical energy	        potential energy

Often in these questions you will be given the rate of flow of water i.e. how many kilograms flow each second. This gives you two pieces of information, mass and time.

1.	How much potential energy could be converted into electrical energy when 200 kg of water falls 40 m into a turbine attached to a generator?

2.	How much energy is stored in a pumped storage hydroelectric scheme if 6 000 kg of water is pumped up 210 m to a reservoir at night time when there is a surplus of electricity?

3.	In a hydroelectric power station 400 kg of water flow each second through the turbines of the power station from a loch 200 m above the turbines.

(a)		How much potential energy is lost by the water each second?

(b)		How much electrical energy could be generated each second assuming that 		there are no energy losses?

(c)		What would the output power of this station be?

4.	A small reservoir is situated 120 m above a hydroelectric power station. The station gives an output power of 2·25 MW.

(a)		How much electrical energy is generated each second in this power station?

(b)		How much potential energy must the water flowing into the turbines lose each 		second in order to generate this electricity?

(c)		What mass of water must flow each second through the turbines of the power 		station in order to generate 2·25 MW of electricity?

5.	The generator of a hydroelectric power station produces an output power of 1·1 MW. Water flows at a rate of 300 kg per second from the loch above the power station.

(a)		How much electrical energy is generated each second?

(b)		How much potential energy must be converted into electrical energy each 			second?

(c)		How high is this loch?

6.	(a)		How much energy is stored in the reservoir of this hydroelectric scheme if it 		contains 200 000 kg of water?

(b)		If all this water flows into the turbines attached to the generators in

1 hour what would the output power from this station be?

7.	2·4 x 106 kg of water flow from a loch 150 m high in 8 hours. What power could this water generate in a hydroelectric power station?

8.	An electric pump is required to fill a reservoir with 1·6 x106 kg of water in 6 hours. The reservoir is 40 m above the pump house.

(a)		How much potential energy must the water gain in 6 hours?

(b)		How much electrical energy must the pump receive in the 6 hours?

(c)		Calculate the power of the pump.

9.	In a model pumped storage hydroelectric power station an electric pump is used to lift water through a height of 1 m. The pump is connected to a 12 V supply and draws a current of 2 A.

(a)		How much electrical energy does the pump use each second?

(b)		How much potential energy could this pump give to the water each second?

(c)		What mass of water can the pump lift each second?

10.	A 230 V pump drawing a current of  3 A is required to lift 200 kg of water through a height of 7 m .

(a)		How much potential energy will the water gain?

(b)		How much electrical energy must be provided to the pump?

(c)		How long will it take for the pump to lift all the water?

Helpful Hint

The energy required to heat materials is often produced by an electrical heater.

Substituting  P = I V    into  	E = P t       gives	E = I t V

where		E = energy on joules (J)

P = power in watts (W)

t =  time in seconds (s)

I =  current in amps (A)

V  =  voltage in volts (V)

You can also use the principle of conservation of energy to solve problems where an electrical heater is used. You studied the “Heat” equations in the previous unit, “Dynamics & Space”:

Eh = Pt = cm(T				Eh = Pt = mL

Eh = ItV = cm(T				Eh = ItV = mL

Use the principle of conservation of energy to solve the following:

11.	How long would it take a 50 W immersion heater to heat 2 kg of water from 10 oC to    80 oC?

12.	How long would it take for a 2 kW kettle to heat 800 g of water from 40 oC to 100 oC?

13.	A 100 W heater is used to heat a 4 kg block of lead. If the heater is left on for

10 minutes calculate the rise in temperature of the block of lead.

14.	Calculate the power of an immersion heater which takes 20 minutes to heat 4 kg of water by 60 oC.

15.	An electric heater operates at 12 V and takes a current of 3 A. It is used to boil alcohol. Calculate the mass of alcohol the heater could evaporate in 20 minutes.

16.	A kettle operating at mains voltage draws a current of 9(6 A. This kettle evaporated 290 g of water at 100 oC in a time of 5 minutes. What value does this give for the specific latent heat of vaporisation of water?

17.	600 g of water was supplied with 163 020 J of heat. Energy losses were negligible.

(a)		What was the change in temperature of the water?

(b)		If heat was supplied to the water at a rate of 543·4 joules per second, how long

did it take to heat the water?

18.	The temperature of 2 kg of steel is raised by 10 0C. It takes 3 minutes for an electric heater connected to the mains (230 V) to do this.

(a)		What is the minimum energy supplied to the steel?

(b)		Assuming no energy losses, what is the power rating of the heater?

(c)		What current is drawn by the heater?

19.	A 500 g mass of copper is heated by a 40 W immersion heater while a 500 g mass of steel is heated by a 50 W heater. The initial temperature of each block is 20 0C. Which block is the first to reach a temperature of 80 oC? You can assume that there are no energy losses.

20.	80 g of alcohol at 20 0C is heated by an electric heater for 6 minutes until it reaches its boiling point of 65 oC. The heater operates at 230 V and draws a current of 125 mA.

(a)		How much electrical energy is used by the heater?

(b)		How much heat energy is absorbed by the alcohol?

(c)		How much energy was ‘lost’ to the environment?

16.  Energy Exam Style Questions

1.	A cyclist is travelling at 10 m s−1 along a level road. The cyclist applies the brakes and comes to rest in a time of 5 s. The combined mass of the cycle and cyclist is 80 kg. The maximum energy converted to heat by the brakes is

A	 160 J

B	400 J

C 	800 J

D 	4000 J

E 	8000 J.

- A ball of mass 0∙50 kg is released from a height of 1∙00 m and falls towards the floor.

Which row in the table shows the gravitational potential energy and the kinetic energy of the ball when it is at a height of 0∙25 m from the floor?

- The length of runway required for aircraft to lift off the ground into the air is known as the ground roll.

The ground roll of an aircraft varies for each take-off.

Use your knowledge of physics to comment on why the ground roll of an

aircraft varies for each take-off.

18.  Electronic Systems – Output Devices

1.	Which of the components in the list below are output devices?

bulb		thermistor		relay		thermocouple

solenoid	loudspeaker		dynamo	LED

LDR		buzzer			motor 		microphone

2.	Which output device could be used in a central locking system of a car?

3.	What would be an appropriate output device for a public address system?

4.		Select an output device which could be used to raise and lower blinds automatically in 	a luxury flat.

5.	Which output device is useful for digital displays on hi-fi systems?

6.	Draw the symbol for each of the output devices you identified in question 1.

19.  L.E.D Circuits

1.	Which of the following LED’s will light?

Helpful Hint

When applying this equation remember that the supply voltage is shared between the LED and the resistor.

Example

A certain LED takes a current of 10 mA and it requires a voltage of 2 V. What should be the value of the series resistor when a supply voltage of 5 V is used?

1st. Sketch the circuit				2nd. Calculate the voltage across resistor R.

2.	Use the stages outlined on the previous page to find the missing values in the 	following table.

Vsupply

|  | Vsupply (V) | Voltage across LED (V) | Current (A) | Voltage across R (V) | Resistance of R (() |
| --- | --- | --- | --- | --- | --- |
| (a) | 6 | 2·0 | 0·010 |  |  |
| (b) | 12 | 2·0 | 0·010 |  |  |
| (c) | 8 | 1·8 | 0·016 |  |  |
| (d) | 20 | 1·6 | 0·008 |  |  |
| (e) | 4 | 1·5 | 0·020 |  |  |
| (f) | 11 | 2·0 | 0·012 |  |  |

3.	For each of the following circuits calculate the value of the series resistor which will enable the LED to operate at its ideal voltage and current.

(a)					(b)

(c)					(d)

(e)					(f)

(g)					(h)

4.	Consider the following circuit.

(a)	Calculate the voltage across the 400 ( resistor.

(b)	Calculate the voltage across the LED.

5.	For the circuit shown below work out the value of the supply voltage which will enable the LED to operate at its stated rating.

6.	The voltage and current specifications for a certain LED are 1·75 V and 10 mA respectively. What should be the value of the series resistor if the LED is powered by a  6 V supply?

7.	Calculate the ammeter reading in the following circuit.

8.	Calculate the voltmeter reading in the circuit shown below.

9.	What is the supply voltage for the following circuit?

10.	Calculate the value of resistor R in the circuit below.

20.  Electronic Systems – Input Devices

In this section you can use the equation:

where		V = voltage in volts (V)

I = current in amps (A)

R = resistance in ohms (( ).

Helpful Hint

When choosing an input device for an electronic system, think about what type

of energy the device has to detect.

capacitor			microphone		photovoltaic cell 	thermocouple 		thermistor		light dependent resistor (LDR)

1.	Select from the list above a suitable input device for each of the following:

(a)	Public address system in a railway station

(b)	Digital thermometer

(c)	Photographers light meter

(d)	Time delay circuit for courtesy lights in a car

(e)	Pilot light flame detector in a gas central heating system

(f)	Sunlight hours recorder at a weather station.

2.	The circuits below show two identical LDR’s each connected to a 6 V supply.

One LDR is placed in a cupboard and the other is placed beside a window.

Circuit (i)						Circuit (ii)

(a)	Calculate the resistance of each LDR.

(b)	State which circuit shows the LDR in the cupboard.

3.	The following circuit shows a thermistor connected to a 5 V supply and placed in a school laboratory.

One morning the ammeter gave a reading of 1·25 mA. Later in the same day the reading had risen to 2·5 mA.

(a)	Calculate the resistance of the thermistor in the morning.

(b)	State what happened to the temperature in the room during the day?

Explain your answer.

4.	The following information for an LDR was found in a components catalogue.

| Light Source | Illumination (lux) | Resistance (k() |
| --- | --- | --- |
| moonlight | 0·1 | 10 000 |
| 60 W bulb at 1m | 50 | 2·4 |
| fluorescent light | 500 | 0·2 |
| bright sunlight | 30 000 | 0·02 |

This LDR is connected to a 12 V supply with an ammeter in series as shown in the 	diagram.

(a)	Determine the resistance, in ohms, of the LDR when exposed to fluorescent 		light?

(b)	Calculate the ammeter reading when a lamp with a 60 W bulb is placed 1 m 		away from the LDR?

(c)	For one source, he ammeter gives a reading of 0·6 A. Determine which light 		source is being used.

5.	A pupil uses a thermistor as a simple electronic thermometer. She connects the thermistor to an ammeter and places the thermistor into a beaker of hot water. The ammeter gives a reading of 8 mA.

| Temperature (oC) | Resistance (() |
| --- | --- |
| 20 | 3 750 |
| 40 | 198 |
| 60 | 750 |
| 80 | 350 |
| 100 | 200 |

(a)	Determine the temperature of the water in the beaker?

(b)	The pupil adds some more water to the beaker and the ammeter gives a new 		reading of 1·6 mA. Determine whether the pupil added hot or cold water to the 		beaker.

(c)	Calculate the new temperature of the water.

(d)	Determine the ammeter reading when the water reaches boiling point.

21.  Potential Divider Circuits

In a series circuit the supply voltage is divided up between the components in the circuit

i.e.

From Ohm’s law we know that since current is constant in a series circuit, the higher the resistance of a component the greater the potential difference across it.

This idea is used in the following example to calculate the potential difference across components in a ‘potential divider’ i.e. series circuit.

Example

Use the fact that the voltage ‘split’ across each component is in the same ratio as the resistance of each component.

V1 	=	R1 x Vs			V2	=	R2 x Vs		where Rt = total resistance

Rt					Rt

= 	4 x 24				= 	8 x 24

12				 	12

=	 8V				=	16 V

( Remember  to check your answer e.g. does V1 + V2  =  Vs  )

Lastly!

Circuit problems in electronics are usually drawn slightly differently than you are used to seeing.

e.g.

Find the potential difference across each resistor in the following circuits:

(1)					    (2)				(3)

(4)					    (5)				(6)

(7)					    (8)				(9)

(10)				   (11)			           (12)

(13)				(14)				(15)

(16)				(17)				(18)

(19)				(20)

Helpful Hint

LDR’s and thermistors often make up part of a potential divider circuit in electronic systems.

It is important to remember that the resistance of these components varies with external conditions.

Use the following data to answer questions 21 – 25.

The tables below show how the resistances of a certain LDR and thermistor vary with

external conditions.

LDR						       Thermistor

| light condition | resistance () |
| --- | --- |
| dark | 10 000 |
| light | 2 500 |
| bright | 20 |

| temperature (oC) | resistance () |
| --- | --- |
| 10 | 4 000 |
| 40 | 1 980 |
| 100 | 200 |

21.	The following circuit is part of the input to an electronic frost alarm.

Calculate the potential difference across the thermistor when it is

(a)	10 o C

(b)	40 o C

22.	The following circuit could be part of a light meter for a camera.

Use the information above to find the potential difference across the LDR when it is:

(a)	dark

(b)	light

23.	Calculate the potential difference across the resistor in the following circuit when the temperature is:

(a)	100 o C

(b)	  40 o C

24.	A young engineer designs part of an electronic system to trigger an alarm when it gets too bright.

Determine the ‘trigger voltage’ across the resistor in the following system when the light level becomes ‘bright’.

25.	Determine the temperature at which the following voltmeters will show identical readings.

Helpful Hint

In a circuit like the following:

You are often required to calculate the “potential” at point X

This is the same as the voltage (or potential difference) across resistor R2 .

Calculate the potential at X in questions 26 - 30.

26.					27.				28.

Switch open		     Capacitor uncharged         		Switch closed

29.						30.

Capacitor fully charged	     	      Switch open.

22.  Transistor Basics & Switching Circuits

1.	Draw the symbol for the npn transistor and label each terminal.

2.	For what do the letters MOSFET stand?

3.	Draw the symbol for the n-channel enhancement MOSFET and label each terminal.

4.	Transistors can be used as switches that are controlled by a voltage.

(a)	State the switching voltage for the npn transistor.

(b)	State the switching voltage for the n-channel enhancement MOSFET.

5.	On your diagrams for questions 1 and 3, indicate where this “switching voltage” 	should be.

Helpful Hint

A transistor operates as a switch in a circuit. An npn transistor switches ‘ON’

when the voltage across XY, in the diagram below, is above approximately 0·7 V.

For the n-channel enhancement MOSFET, this switching voltage is approximately 2V.

In the last section you studied potential dividers. A potential divider is usually

placed between P and Q. Various components can be used to make up the potential

divider but it is always the potential difference across XY which switches on or

off the transistor.

Some examples are shown on the next page.

Examples for the NPN Transistor

(a)	The potential divider can be two resistors in series

(b)	The potential divider can be a Potentiometer

(c)		The potential divider may contain a sensor  (the words in bold will 	change depending on the type of sensor and its position in the potential 	divider.)

1.	For each of the following circuits calculate the potential difference across XY and then state whether the output device is ON or OFF.

(a)

(b)

(c)

(d)

(e)

(f)	(Hint! Think here!)

2.	Consider the following circuit.

(a)	What is the voltage across XY when the sliding connection is at point A?

(b)	Does the LED light when the sliding connection is at point A?

(c)	Does the LED light when the sliding connection is at point B? Explain your

answer.

(d)	Does the LED light when the sliding connection is at point C? Explain your

answer.

3.	The following circuit is used to switch on an electric heater automatically when the

temperature in a room falls below a certain value.

(a)	Explain how the circuit operates.

(b)	What would be the effect of decreasing the resistance of the variable resistor?

(c)	Why would it be unsuitable to put the heater at point X instead of the relay?

4.	Study the four circuits shown below.

(a)	Which circuit could be used to remind drivers at night to put on their

headlamps? Explain your answer.

(b)	Which circuit would be useful as a warning indicator of low temperature in an 		elderly person’s house? Explain your answer.

(c)	Which circuit could be used to waken campers when daylight arrives? Explain 		your answer.

(d)	Which circuit would be most suitable as a fire alarm?

5.	For each of the following circuits state whether the output device is ON or OFF and 	explain your answer.

(a)					          (b)

(c)						(d)

(e)						(f)

23.  Pressure, Force and Area

In this section you can use the equation:

P   =      F

A

Where		P  =  pressure in pascals (Pa) or newtons per square metre (Nm-2)

F  =  force in newtons (N)

A  =  area in square metres (m2)

1.	Find the missing values in the following table.

|  | Pressure (Pa) | Force (N) | Area (m2) |
| --- | --- | --- | --- |
| (a) |  | 120 | 1.6 |
| (b) |  | 4000 | 0.5 |
| (c) | 1.1 x 105 |  | 2.0 |
| (d) | 9000 |  | 8.0 x 10-2 |
| (e) | 12 000 | 7.2 x 105 |  |
| (f) | 1.4 x 104 | 4.9 x 104 |  |

2.	An elephant can exert a force of 5000 N by pressing his foot on the ground. If the 	area of his foot is 0.02 m2, calculate the pressure exerted by his foot.

3.	A water tank has a weight of 9 800 N and a base area of 20 m2. It sits on a floor. 	Calculate the pressure exerted by the tank on the surface of the floor.

4.	A syringe has a piston with a cross-sectional area of 2 x 10-4 m2. The piston is pushed 	with a force of 12 N. Calculate the pressure.

5.	A drawing pin has a sharp point with an area of 1x 10-8 m2. Calculate the pressure 	exerted by the point when the head is pushed with a force of 8 N.

6.	Explain why the use of large tyres helps to prevent a tractor

from sinking into soft 	ground.

7.	If you want to rescue someone who has fallen through ice on a pond, would it be 	easier to walk or crawl across the ice towards him? Explain why.

8.	A 0.48 kg tin of baked beans is a cylinder with a radius of 3.2 x 10-2 m. It is placed on 	a kitchen counter.

(a)	Calculate the weight of the tin. This is the force it exerts on the counter.

(b)	Calculate the area of the tin in contact with the counter.

(c)	Calculate the pressure on the counter caused by the tin.

9.	A television has a length of 1.24 m, a height of 0.93 m and a depth of 0.08 m.

The mass of the television is 30 kg and it sits on a table.

(a)	Calculate the weight of the television. This is the force it exerts on the table.

(b)	Calculate the area of the television in contact with the table.

(c)	Calculate the pressure on the table caused by the television.

10.	A car of mass 1250 kg is driven on to a bridge. The pressure on the surface of the 	bridge when all four tyres are on the ground is 39.0 kPa.

(a)	Calculate the weight of the car.

(b)	Calculate the total contact area of the car’s tyres on the bridge.

(c)	Determine the contact area of one tyre.

11.	A 50 kg ballerina can exert a pressure of 2.2 x 106 Pa

when she stands on one pointed foot. Determine the area

of the point of her ballet shoe. (Remember to calculate

the weight of the ballerina first!)

12.						A tank exerts a pressure of  only  3.675 x 104 Pa 						on the ground due to the large surface area of its 						tracks which is 8 m2.

(a)	Calculate the weight of the tank. This is 							the force it exerts on the ground.

(b)	Calculate the mass of the tank.

13.	The surface area of a person’s head is approximately 0.5 m2. Calculate the force 	exerted by the air on the person’s head, given that air pressure is 1 x 105 Pa.

14.	Measuring the total weight of yourself and your lab stool then measure the contact 	area of one leg of the stool in “swinging position”. Calculate the pressure that is 	exerted on the floor when you swing on your stool.

15.	In an experiment, weights are placed on top of a syringe filled with trapped air.

A Bourdon Gauge is used to measure the air pressure inside the syringe. This is then 	repeated for different weights.  The results are shown in the table.

| Force (N) | Total Pressure (x 105 Pa) | Pressure due to added weight (x 103 Pa) |
| --- | --- | --- |
| 0 | 1.01 | 0 |
| 1 | 1.03 | 2 |
| 2 | 1.05 | 4 |
| 3 | 1.07 | 6 |
| 4 | 1.09 | 8 |
| 5 | 1.11 | 10 |

Use this data to construct a line graph of force against pressure due to the added 	weight, and use the gradient of the straight line to calculate the surface area of the 	plunger inside 	the syringe.

24.  Kinetic Theory of Gases

1.	Explain what is meant by the following terms, in relation to a gas:

(a)	volume

(b)	temperature

(c)	pressure

2.	Air is trapped inside a conical flask, as shown below, and the flask is heated.

The temperature and the pressure of the trapped air are monitored as the air is heated.

The results are shown in the table.

| Temperature (°C) | Pressure (x 105 Pa) |
| --- | --- |
| 20 | 1.01 |
| 30 | 1.04 |
| 40 | 1.08 |
| 50 | 1.11 |
| 60 | 1.15 |
| 70 | 1.18 |

- Using the data, draw a line graph of pressure against temperature (in degrees 	Celsius). Make sure that your temperature axis goes from -300 °C to 70 °C.

- On your graph from part (a), continue your straight line back until it crosses 	through the x-axis. At what temperature would the pressure of the gas reach 	zero?

- Explain why the temperature you determined in part (b) is known as “absolute 	zero”.

- Explain, using the kinetic theory of gases, why the air pressure increases as the 	temperature increases.

3.	The following apparatus is designed to investigate how changing the volume of 	trapped air will affect the pressure of the trapped air.

Air is trapped above a pillar of oil and its volume can be measured using a scale on 	the pillar. The pressure of the air can be measured with the Bourdon Gauge.

The pump is used to raise the level of oil and reduce the volume of air.

It is observed that, as the volume of trapped air decreases, the pressure increases.

In fact, it is found that, provided the temperature remains constant, the pressure is 	inversely proportional to the volume.

P    1 / V

Use the kinetic theory of gases to explain this result.

4.	Explain, using the appropriate gas law, why a balloon will burst if you squeeze it.

5.	In an experiment, an open capillary tube with a mercury thread is placed in to a heat 	bath.

As the temperature of the gas increases, the mercury thread moves up the capillary 	tube.

The pressure of the gas remains constant because the capillary tube is open.

The temperature of the gas is measured with a thermometer and the volume of the gas 	is measured using a scale next to the open capillary tube. The results of the 	experiment are shown.

| Temperature (°C) | Temperature (K) | Volume (cm3) |
| --- | --- | --- |
| 20 |  | 1.50 |
| 25 |  | 1.88 |
| 30 |  | 2.25 |
| 35 |  | 2.63 |
| 40 |  | 3.00 |
| 45 |  | 3.38 |

- Copy the table and complete it to show the temperatures in Kelvin.

- Draw a line graph of volume against temperature (in Kelvin).

- What conclusion can you make from this graph?

- Explain this result in terms of the kinetic theory of gases.

25.  The Gas Laws

In this section you can use the gas equations:

P1V1 = P2V2                 			 P1   =   P2			          V1   =   V2

T1        T2			          T1         T2

Together these equations form the General Gas Equation:

P  V   =   constant	       or   		P1V1   =   P2V2

T					 T1            T2

Where		P  =  pressure in pascals (Pa) or atmospheres (atm)

V  =  volume in cubic metres (m3) or litres (l) … or any suitable unit

T = temperature in KELVIN (K)

Kelvin temperatures must be used in these calculations.

REMEMBER:

- KELVIN is ALWAYS GREATER  by 273.

- KELVIN temperatures are ALWAYS POSITIVE.

- A change in temperature in Kelvin is the same as a change in temperature in degrees Celsius.

1. 	Convert the following temperatures from °C to Kelvin.

(a)  27°C 		(b) 100°C 		(c) 0°C 		(d) -50°C

2. 	Convert the following temperatures from Kelvin to °C.

(a) 400K 		(b) 10K 		(c) 273K 		(d) 97K

3.	The temperature of water  in a beaker rises from 20 oC to 80 oC.

(a)	Calculate this change in temperature in oC.

(b)	Calculate this change in temperature in K.

Pressure & Volume

4. 	A sealed syringe contains 100 cm3 of gas. The gas in the syringe has a pressure of

105 kPa. The syringe plunger is pushed in to a new volume of 50 cm3.

Calculate the new pressure of the gas.

5.	In an experiment the temperature of a fixed mass of gas is kept constant. The 	volume is altered and various readings of pressure and volume are taken. These are 	shown below.

Without drawing a graph, but buy using all of the data, what conclusion can you 	make from these results?

Volume (cm3)		45	39	37	34	25	22	18

Pressure (kPa) 	101	116	122	135	180	210	250

6.	A fixed mass of gas is kept at constant temperature but the pressure is increased from 	1.01 x 105 Pa to 3.00 x 105 Pa.

The initial volume was 0.2 m3. Determine the final volume.

7.	A weather balloon contains 100 m3 of helium when atmospheric pressure is 90 kPa. If 	the atmospheric pressure changes to 100 kPa calculate the new volume of helium at 	the same temperature.

8.	A 5 cm3 syringe is filled with air and the pressure of the air is found to be

1.01 x 105 Pa. The syringe plunger is then pushed until there is 3 cm3 of air. Calculate 	the new air pressure.

9.	A scuba diving air tank has a volume of 7.5 litres and is filled with air at a 	pressure of 1.21 x 107 Pa. Determine the volume this air would occupy 	at atmospheric pressure (1.01 x 105 Pa).

Pressure & Temperature

10. 	A glass flask contains a fixed volume of gas. The pressure of the gas is 114 kPa when 	the temperature is 27°C.

Calculate the new pressure of the gas when the temperature is reduced to 0 °C.

Remember to change your temperatures to Kelvin!

11.	The pressure of a fixed mass of gas is 200 kPa at 40 ºC and the volume is 1.5 m3. The 	temperature is increased to 100 ºC but the volume remains the same. Calculate the 	new pressure.

12.	The pressure of air in a car tyre is 2.5x105 Pa at a temperature of 27 ºC. After a 	motorway journey the pressure has risen to 3.0x105 Pa. Assuming the volume of air in 	the tyre has not changed, calculate the resulting temperature of air in the tyre.

13.	At a temperature of 20 °C, the pressure of a fixed mass of gas in a sealed container is 	found to be 104 kPa. The gas is heated to a uniform temperature of 90 °C using a heat 	bath. Calculate the pressure of the gas at a temperature of 90 °C.

14.	The pressure of the air in a lorry tyre is found to be 2.58 x 105 Pa at the end of a 	journey. Once the tyre has cooled down, the temperature of the air inside the tyre is 	found to be 10 °C with the pressure decreasing to 2.41 x 105 Pa.

Calculate the temperature of the air in the tyre at the end of the journey.

Temperature & Volume

15.

A sealed syringe has a volume of 30 ml when the temperature of the gas in the syringe 	is 15°C.

Calculate the new volume of the gas when the temperature is changed to 30°C.

16.	The volume of a fixed mass of gas is 40.0 cm3 at 20 °C. The temperature of the gas is 	increased to 40 °C without changing the pressure.

A student makes this statement:

‘As the temperature of the gas has doubled, the volume of the gas will also double. 	Therefore, the volume of the gas at 40 °C will be 80.0 cm3.’

(a)	Explain why this statement is incorrect.

(b)	Calculate what the volume of the gas would actually be at 40 °C.

17.	Air is trapped in a glass capillary tube by a bead of mercury. The volume of air is 	found to be 0.15 cm3 at a temperature of 27 °C.

Assuming that the pressure of the air remains constant, what is the volume of the air 	at a temperature of 87 °C?

Pressure, Temperature & Volume

18.	A fixed mass of gas is trapped in a syringe. The gas 	has a 	pressure of 1.63 x 105 Pa when it has a volume of 3.0 cm3 	and a temperature of 22 °C.

The gas is then heated until it has a uniform temperature 	of 57 °C and a volume of 5.0 cm3.

Calculate the new pressure of the gas.

26.  Applications of The Kinetic Model of a Gas

1.	Explain why the pressure in car tyres increases as more air is pumped in.

2.	Explain why car tyres are marked with a maximum pressure limit.

3.	The air pressure decreases, the higher we go from the surface of Earth.

(a)	Explain why aircraft cabins must contain pressurised air.

(b)	Predict and explain what might happen  if an explosion happened on an 			aeroplane at 40 000 feet, blowing open a door.

4.	The summit of Mount Everest is at 8848 m. At this height the air pressure is 	approximately one third of the air pressure at sea level. In addition, the temperature at 	the summit of Everest averages around – 19oC in summer, dropping to -36oC in 	winter.

(a)	Use your knowledge of temperature and pressure to explain why you think it 		is very 	difficult to survive for very long at this altitude.

(b)	Research what the main health risks are for high altitude climbers, due to the 		drop in air pressure.

5.	Read the information below and overleaf and use it to answer the questions that 	follow:

The Dangers of Scuba Diving

As scuba diving is a popular recreational sport, beautiful coral reefs and eerie 	shipwrecks around the world have become major tourist draws in their own right. 	However, it should not be forgotten that scuba diving is an extreme sport with its own 	peculiar injuries and potentially life-threatening hazards. Most of these scuba diving 	dangers stem from the effects of the increased water pressure of the undersea 	environment, but there are also dangers posed by sea life and faulty equipment.

## Barotrauma

Barotrauma is caused by the damage done by increased underwater pressure on the air pocket in the middle ear. Divers usually "equalize" during a dive by pinching their nose shut and blowing, by chewing or by swallowing to push more air into the middle air. However, a descent that is too fast can result in severe pain and even injury to the middle ear.

## Decompression Sickness

Often called "the bends," decompression sickness is caused by increased underwater pressure causing the body's tissues to absorb more nitrogen. If that pressure is suddenly reduced, this extra nitrogen forms potentially harmful bubbles. Deep divers return to the surface in carefully monitored stages so as to control the rate at which this absorbed nitrogen is released. A case of the bends can range from aching joints or a skin rash to paralysis and death.

## Nitrogen Narcosis

Another nitrogen-related danger is the narcotic effect of all that extra nitrogen in the body. Nitrogen narcosis is a danger because it impairs judgement and sensory perception. As with the bends, the degree of nitrogen narcosis is related to how deep a diver goes and how much nitrogen they absorb.

## Oxygen Toxicity

Oxygen toxicity is usually a problem only encountered by deep divers who go below 135 feet. The body absorbs extra oxygen under increased underwater pressure. For most divers this is not a problem, but at extreme depths so much extra oxygen is absorbed that this life-giving gas becomes a poison. The effects range from tunnel vision and/or nausea to twitching to loss of consciousness and/or seizures.

## Pulmonary Embolism

Another risk facing a diver who rapidly ascends to the surface is pulmonary embolism. The increased pressure of the undersea environment results in extra gas being crammed into the same lung space. A rapid rise to the surface can cause the lungs to swell and even pop like a balloon because the water pressure decreases. Scuba divers guard against pulmonary embolism by making slow, controlled ascents to the surface and by never holding their breath.

## Sea Life

Divers should never forget that each dive is the equivalent of entering an untamed wilderness. While most sea creatures are not aggressive towards divers and attacks are extremely rare, incidents do happen and a diver cannot afford to forget that she is surrounded by wild animals. The famed TV wildlife host "Crocodile Hunter" Steve Irwin was killed in 2006 when he was stung through the chest by a stingray, a frequently encountered and usually harmless sea creature. Divers should always treat sea life with great care and respect.

## Defective Equipment

Many casual scuba divers do not own their own equipment, and are therefore reliant on renting equipment from the scuba diving operator who is conducting their dive trip. A broken depth gauge could lead to a mild case of decompression sickness, while a bad regulator might result in drowning. A diver should always thoroughly check rented scuba diving equipment, and never be shy about asking for a new piece of gear if they suspect something is wrong with what they have.

Questions

1.	Which part of the body can be damaged by “barotrauma”?

2.	How can a diver prevent or reduce the effect of barotrauma?

3.	What is the scientific  term for “The Bends”?

4.	“The Bends” is caused by the body absorbing which gas?

5.	What other condition can be caused by the body absorbing too much of the gas in Q. 4?

6.	In high pressure environments, like deep sea, the body can absorb too much oxygen. What are 	the effects of this?

7.	If a diver gets into difficulty underwater, should the diver swim to the surface as quickly as 	possible? Explain your answer.

8.	Apart from the dangers due to the change in water pressure, name two other hazards that 	might face a diver.

# Text boxes

TRANSISTORS

NPN

MOSFET

charge = current x time

Q = I t

12V

+

-

+

-

-

+

3000V

5000V

0V

500V

-250V

+150V

+300V

-500V

12V

0V

X

12V

0V

X

4V

Y

12V

Y

6 V

6 V

6 V

6 V

0 V

0 V

0 V

0 V

Y

X

6 V

6 V

6 V

6 V

0 V

0 V

0 V

0 V

Y

X

oscilloscope

oscilloscope

A

R

R

2·5 V

2·5 V

12 V

D

B

C

A

36 V

12 V, 36 W

R

15 V

200 (

100 (

14 V

R2

12 V

R1

0·2 A

0·3 A

L1

L2

R1

6 V

4 A

230 V

S2

12 V

S1

L1

L2

H2

H1

C

B

A

H1

230 V

M

H2

24 V

R = 900(

Circuit 1

Circuit 2

voltage = current x resistance

V = IR

Vs

Vs

Vs

50 mA

2·56 A

10 A

480 (

250 (

5 (

I

I

I

12 (

550 (

50 (

660 (A

30 (A

25 mA

R

R

R

Rs = R1 + R2 + R3 +......

R1

R2

R3

800 (

5 k(

3·2 k(

950 (

R

6·3 k(

+

+

=

+  ....

120 (

120 (

20 (

20 (

80 (

80 (

400 (

1 600 (

100 (

150 (

80 (

120 (

800 (

2 400 (

150 (

300 (

300 (

600 (

1·2 k(

600 (

600 (

600 (

600 (

600 (

3 k(

3 k(

3 k(

3 k(

900 (

600 (

300 (

600 (

200 (

280 k(

560 k(

560 k(

R

220 (

1 232 (

300 (

A

900 (

1 200 (

X

1 800 (

Helpful Hint

Rs	=	R1 + R2 + R3 +......	( for a series section of a circuit)

1	=	1  +  1  +  1  +......	(for a parallel section of a circuit)

Rp		R1    R2     R3

60 (

40 (

60 (

10 (

20 (

20 (

15 (

30 (

15 (

30 (

10 (

10 (

10 (

10 (

10 (

5 (

5 (

10 (

10 (

10 (

100 (

100 (

250 (

250 (

560 (

560 (

Y

Z

X

80 (

40 (

60 (

80 (

120 (

90 (

90 (

90 (

15 (

90 (

15 (

10 (

100 (

100 (

50 (

50 (

10 (

power  = energy

time

P = E

t

power = current x voltage

P = I V

12 V

A

24 W

BL300

360 W

230 V	50/60 Hz

made in the U.K

I = 4·2 A

1 kW

P = I V    and     V  =  I  R

3 A

12 V

A

10 k(

V

A

A

V

V

Circuit 2

Circuit 1

Type KE	180		Serie 2

Power 2200W

230 V       50 - 60 Hz

2·2 kW

B3

(

(

8 V

12 V

B1

B2

(

16 V

24 V

R2

R3

R1

(

I = 2 A

12 V

(

(

I = 0·9 A

36 V

D

C

A

B

20 (

20 (

Network 1

20 (

20 (

90 (

90 (

5 (

turbine		generator				turbine		generator

turbine		generator				turbine		generator

Water pumped

back up

Water flows down

water falls through a height of 150 m

A

F

E

D

C

B

When working with LED circuits you can use the equation:

V  =  I R

5 V

VR  =  Vsupply - Vled

=    5  -   2

=      3 V

I = 10 mA

= 0·010 A

R

3rd.  Apply V = IR to find the value of R

VR  =  3 V		VR  =  I R

I     =  0·01 A		3    =   0·01 x R

R    =   ?		R   =   3  /  0·01

R   =   300 (

R

(2V(

R

(VR(

I

(Vled(

9 V

1·8 V,

12 mA

R

4 V

2·1 V,

10 mA

R

6 V

1·6 V,

11 mA

R

12 V

2·2 V,

10 mA

R

9·8 V

(2·3 V(

15mA

R

S1

H2

H1

L2

L1

S3

S2

20mA

9·5 V

(3 V(

R

10mA

5·1 V

400 (

8mA

800 (

2·2 V,

11 mA

12 V

(1·8 V(

2 040 (

A

6 V

475 (

V

8mA

1 200 (

3V

15mA

9 V

R

20mA

4V

V = IR

6 V

6 V

0·03 A

0·0024 A

A

5 V

12 V

A

6 V

A

Vs	=	V1 + V2

where		Vs = supply voltage

V1 = voltage across R1

V2 = voltage across R2

Vs

R1

R2

(V1(

(V2(

24V

8(

4(

+ 24 V

24 V

8 (

would be drawn as

8 (

4 (

4 (

0 V

+ 36 V

0 V

+ 12 V

0 V

10 (

10 (

+ 24 V

0 V

6 (

6 (

3 (

3 (

+ 12 V

0 V

10 (

2 (

+ 10 V

0 V

6 (

4 (

+36 V

0 V

16 (

20 (

+ 24 V

0 V

4 (

8 (

+ 24 V

0 V

5 (

10 (

+ 24 V

0 V

18 (

36 (

+ 36 V

0 V

3 (

9 (

+ 36 V

0 V

4 (

12 (

+36 V

0 V

7 (

21 (

+ 5 V

0 V

3 k(

2 k(

+ 240 V

0 V

434 (

62 (

+ 36 V

0 V

25 (

15 (

+ 20 V

0 V

100 (

22 (

+ 24 V

0 V

180 (

36 (

+ 12 V

0 V

3 (

6 (

+ 10 V

0 V

120 (

40 (

+ 240 V

0 V

144 (

36 (

+ 230 V

0 V

100 (

+ 12 V

0 V

1 k(

+ 24 V

0 V

500 (

+ 36 V

0 V

1·5k(

+ 230 V

0 V

V1

200 (

V2

X

+ 5 V

R1

R2

0 V

X

+ 12 V

0 V

20(

X

+12 V

0 V

10 k(

X

+ 5 V

0 V

3·5 k(

X

+ 36 V

0 V

1 k(

X

+ 5 V

0 V

65(

0·7 V

P

Q

X

Y

X

10 (

10 (

6 V

+ 6 V

X

Y

0 V

Voltage across XY is 6 V so transistor conducts and bulb lights.

0 V

+ 6 V

X

Y

0 V

Voltage across XY is 0 V so transistor does not conduct therefore bulb is OFF.

As the temperature increases, the resistance of the thermistor decreases.

So does its voltage.

This means the voltage across XY increases.

Eventually it will be hot enough that this voltage will become greater than 0.7V so the transistor and bulb will switch ON.

+6 V

0 V

Y

V

thermistor

X

X

400 (

400 (

+12 V

0 V

Y

X

800 (

400 (

+6 V

0 V

Y

X

450 (

50 (

Y

+5 V

0 V

X

100 (

400 (

Y

+1·5 V

0 V

X

100 (

3·9 k(

+2 V

0 V

Y

X

10 (

80 (

+4 V

0 V

Y

+ 5 V

mains 230 V

0 V

heater

X

+5 V

0 V

+5 V

0 V

Circuit B

Circuit A

+5 V

0 V

+5 V

0 V

Circuit C

Circuit D

+5 V

0 V

+5 V

0 V

+5 V

0 V

capacitor charged

+5 V

0 V

capacitor uncharged

switch closed

+5 V

0 V

+5 V

0 V

capacitor charged

1.24m

0.93m

0.08m

Bourdon Gauge

1 N

Syringe

Trapped Air

Bourdon Gauge

Thermometer

Heat Bath

Air

Pump

Fixed Mass of air

Bourdon Gauge

Oil

Open Capillary Tube

Thermometer

Heat Bath

Mercury Thread