S1 Unit- 5 Electricity Learning Outcome Checklist

| lesson |  | by the end of each lesson you should know (including meanings of key words) |
| --- | --- | --- |
| 1 |  | There are two types of charge: positive and negative. Like charges repel, opposite charges attract. Electrons are negatively charged particles that carry energy around a circuit. |
| 2 |  | Current is a flow of electrons. A conductor is a material that allows electric current to flow through it easily e.g. metals and carbon An insulator is a material that is poor at conducting electric current e.g. non-metals Current is measured in amperes (A). Electrons flow from negative to positive. The circuit symbol for a cell and a lamp |
| 3 |  | Cells provide electrical energy for other components in a circuit Other components convert electrical energy to other useful energy types. Electricity moves energy from one place to another. Ammeters are used to measure current and are connected in series. The circuit symbol for an ammeter |
| 4 |  | Voltage is a measure of the energy given to electrons Voltage is measured in volts (V). The voltage across components in a series circuit adds up to the supply voltage. Voltmeters are used to measure voltage and are connected parallel to a component. The circuit symbol for a voltmeter. |
| 5 |  | A series circuit has only one path for the current. The current in a series circuit is the same at all points. The voltage across components in series adds up to the supply voltage. |
| 6 |  | Parallel circuits have more than one path for the current to flow round. The sum of the currents in the branches is equal to the current through the supply. Voltages across components in parallel are equal. |
| 7 |  | Resistance is an opposition to electric current. Resistors convert electrical energy into heat energy. The symbols for a resistor and a variable resistor. |
| 8 |  | The position of the live (brown), neutral (blue) and earth (green/yellow stripes) wires in a 3-pin mains plug. the live wire carries high energy current & the neutral wire carries low energy current Household appliances and lights are normally connected in parallel |